SPI_Slave
XulA2-LX9 + StickIt!-MB
with
Raspberry Pi 2B (RPi2B) Master
four wire
MOSI, MISO, SCLK, and SS
04/11/16

Raspberry Pi 2B RPi2B provides connections to the StickIt!-MB which provides the signals needed to communicate with the XulA2-LX9 or XulA2-LX25.

An external led is connected to T4 PM2 Xula2 CH 15 led<0>. Following the loading of the FPGA the external led will blink at 1 per sec. This is currently functioning correctly.

Four signals provide the SPI interface between the RPi2B and XulA2.
Xula2 CH 25 pin 19 GPIO10(SPI_MOSI)
Xula2 CH 24 pin 21 GPIO09 (SPI_MISO)
Xula2 CH 24 pin 23 GPIO11 (SPI_CLK)
Xula2 CH 08 pin 24 GPIO08_CE0

In the build module of the xula2_blinky_spi_slave is where the pins are mapped to RPi2B connector P1.

    brd.add_port_name('led', 'pm2', slice(0, 8))
    #xula2 chan25 BCM10_MOSI ----> RPI_GPIO_P1_19 /* MOSI */
    brd.add_port('mosi', 'F2')
    #xula2 chan24 BCM09_MISO ----> RPI_GPIO_P1_21 /* MISO */
    brd.add_port('miso', 'F1')
    #xula2 chan23 BCM11_SCLK ----> RPI_ GPIO_P1_23 /* CLK */
    brd.add_port('sck', 'H2')
    #xula2 chan08 BCM08_CE0 ----> RPI_GPIO_P1_24 /* CE0 */
    brd.add_port('ss', 'J14')

The above information is what rhea uses to create the xula2.ucf

The rhea package creates several files xula2.v xula2.ucf below.

#
NET "miso" LOC = "F1" ;
NET "led<0>" LOC = "T4" ;
NET "led<1>" LOC = "R1" ;
NET "led<2>" LOC = "M1" ;
NET "led<3>" LOC = "J4" ;
NET "led<4>" LOC = "R2" ;
NET "led<5>" LOC = "M2" ;
NET "led<6>" LOC = "K3" ;
NET "led<7>" LOC = "H1" ;
NET "ss" LOC = "J14" ;
NET "clock" LOC = "A9" ;
NET "mosi" LOC = "F2" ;
NET "sck" LOC = "H2" ;
#
NET "clock" TNM_NET = "clock";
TIMESPEC "TS_clock" = PERIOD "clock" 83.3333333 ns HIGH 50%;
#

In RPi2B bcm2835 library. This is where the pins for the spi are assigned

void bcm2835_spi_begin(void)
{
    volatile uint32_t* paddr;

    /* Set the SPI0 pins to the Alt 0 function to enable SPI0 access on them */
    bcm2835_gpio_fsel(RPI_GPIO_P1_26, BCM2835_GPIO_FSEL_ALT0); /* CE1 */
    bcm2835_gpio_fsel(RPI_GPIO_P1_24, BCM2835_GPIO_FSEL_ALT0); /* CE0 */
    bcm2835_gpio_fsel(RPI_GPIO_P1_21, BCM2835_GPIO_FSEL_ALT0); /* MISO */
    bcm2835_gpio_fsel(RPI_GPIO_P1_19, BCM2835_GPIO_FSEL_ALT0); /* MOSI */
    bcm2835_gpio_fsel(RPI_GPIO_P1_23, BCM2835_GPIO_FSEL_ALT0); /* CLK */

    /* Set the SPI CS register to the some sensible defaults */
    paddr = bcm2835_spi0 + BCM2835_SPI0_CS/4;
    bcm2835_peri_write(paddr, 0); /* All 0s */

    /* Clear TX and RX fifos */
    bcm2835_peri_write_nb(paddr, BCM2835_SPI0_CS_CLEAR);
}

In file spi.c after calling the bcm2835_spi_begin(); above the bit order is set to MSBFIRST

    bcm2835_spi_setBitOrder(BCM2835_SPI_BIT_ORDER_MSBFIRST); // The default
    bcm2835_spi_setDataMode(BCM2835_SPI_MODE0); // The default
    bcm2835_spi_setClockDivider(BCM2835_SPI_CLOCK_DIVIDER_65536); // The default
    bcm2835_spi_chipSelect(BCM2835_SPI_CS0); // The default
    bcm2835_spi_setChipSelectPolarity(BCM2835_SPI_CS0, LOW); // the default

To run the simulation “python xula2_blinky_spi_slave.py –trace” which traces the signals of
def tb(led, clock, mosi, miso, sck, ss, reset=None): and creates the “tb.vcd” file that can be viewed with
“gtkwave tb.vcd”

The RPi2B is set to send MSBFIRST. In the simulation below the signal mosi MSB of the value 0xCE 11001110 is at 9551 ns on the raising edge of the signal sck.

In the simulation below the signal mosi LSB of 0xCE 11001110 is

at 12827 ns the raising edge of the signal sck.

This appears to match the RPi2B sending MSBFIRST.

In addition rhea creates the xula2.tcl file.

#
#
# ISE implementation script
# create: Sun, 10 Apr 2016 12:13:22 +0000
# by: xula2_blinky_spi_slave.py
#
#
# set compile directory:
set compile_directory .
set top_name xula2
set top xula2
# set Project:
set proj xula2
# change to the directory:
cd xilinx/
# set ucf file:
set constraints_file xula2.ucf
# set variables:
project new xula2.xise
project set family spartan6
project set device XC6SLX9
project set package FTG256
project set speed -2

# add hdl files:
xfile add xula2.ucf
xfile add xula2.v
# test if set_source_directory is set:
if { ! [catch {set source_directory $source_directory}]} {
  project set "Macro Search Path"
 $source_directory -process Translate
}
project set "Create Binary Configuration File" "true" -process "Generate Programming File"
 project set "FPGA Start-Up Clock" "JTAG Clock" -process "Generate Programming File"
# run the implementation:
process run "Synthesize"
process run "Translate"
process run "Map"
process run "Place & Route"
process run "Generate Programming File"
# close the project:
project close

Creating a software reset for the XulA2-LX with StickIt!-MB.

SPI_Slave software is provided with rhea package.

from rhea.system import Global, Clock, Reset, FIFOBus, Signals
/home/vidal/wkg/rhea/rhea/system/glbl.py
Global
/home/vidal/wkg/rhea/rhea/system/clock.py
Clock
/home/vidal/wkg/rhea/rhea/system/reset.py
Reset
/home/vidal/wkg/rhea/rhea/system/stream/fifobus.py
FIFOBus
/home/vidal/wkg/rhea/rhea/system/hwtypes.py
Signals
from rhea.cores.spi import SPIBus, spi_slave_fifo
/home/vidal/wkg/rhea/rhea/cores/spi/spi.py
SPIBus
/home/vidal/wkg/rhea/rhea/cores/spi/spi_fifo_slave.py
spi_slave_fifo
from rhea.cores.misc import glbl_timer_ticks
/home/vidal/wkg/rhea/rhea/cores/misc/glbl_timer_ticks.py
glbl_timer_ticks

The StickIt!-MB provides a 3 PMOD connectors a 40 pin connector to the RPi2B. In addition the a socket to support either a XulA2-LX9 or XulA2-LX25 FPGA.

XulA2 mounted on StickIt!-MB.

Create a bit file to make the xula2 FPGA provide a jumper on
 pins 19 GPIO10(SPI_MOSI) & pin 21 GPIO09 (SPI_MISO).

Set the PATH to ISE WEB PACK

. /opt/Xilinx/14.6/ISE_DS/settings64.sh

vidal@ws009:~/wkg/jpeg-2000-test/xula2_fpga/jumper_tests/spi$
python jumper_xula2_spi.py –build

vidal@ws009:~/wkg/jpeg-2000-test/xula2_fpga/jumper_tests/spi$ cp xilinx/xula2.bit xilinx/jumper_spi.bit

vidal@ws009:~/wkg/jpeg-2000-test/xula2_fpga/jumper_tests/spi$
python jumper_xula2_spi.py –build

pi@raspberrypi2-146 ~/bcm2835-1.45/examples/spi $
xsload --usb 0 --fpga ~/jpeg-2000/xula2_fpga/
jumper_tests/spi/xilinx/jumper_spi.bit

pi@raspberrypi2-146 ~/bcm2835-1.45/examples/spi $
gcc -o spi spi.c -l bcm2835

pi@raspberrypi2-146 ~/bcm2835-1.45/examples/spi $ sudo ./spi
Sent to SPI: 0x23. Read back from SPI: 0x23.
pi@raspberrypi2-146 ~/bcm2835-1.45/examples/spi

Appendix C. XulA2-LX25 & XulA2-LX9 freatures.
LX25

LX9

LX25

- Open-source design
- XC6SLX25 FPGA
- 32 MByte SDRAM
- 8 Mbit Flash
- microSD card socket
- 3.3 & 1.2V regulators
- 40-pin interface
- 12 MHz oscillator
- PIC 18F14K50 micro
- USB 2.0 port
- Auxiliary JTAG port
- Works with the XSTOOLs software
- Works with XILINX ISE and WebPACK
- Works with XILINX iMPACT and ChipScope (requires Xilinx JTAG cable)

LX9

- Open-source design
- XC6SLX9 FPGA
- 32 MByte SDRAM
- 8 Mbit Flash
- microSD card socket
- 3.3 & 1.2V regulators
- 40-pin interface
- 12 MHz oscillator
- PIC 18F14K50 micro
- USB 2.0 port
- Auxiliary JTAG port
- Works with the XSTOOLs software
- Works with XILINX ISE and WebPACK
- Works with XILINX iMPACT and ChipScope (requires Xilinx JTAG cable)