Conversion of Verilog
wbdeppsimple.v
With MyHDLto
toplevel.v
05/07/16

The file “my_wbdepp.py” is a Python program that can provide both Verilog or VHDL files. The file “my_wbdepp.y” is found a Appendix A. To create “toplevel.v”. The command to create the file “toplevel.v” from the file “my_wbdepp.py” is “python my_wbdepp.py –convert”. The file “toplevel.v” is at Appendix B. toplevel.v In addition, MyHDL can simulate the Verilog. The command “python my_wbdepp –trace” is used to generate a Value Change DUMP VCD “tb.vcd” . The can be viewed with the command “gtkwave tb.vcd”.

In below simultion the signal “i_rpi2B” was connected to “i_depp” and the “o_rpi2B” is connected to “o_depp”. This is done with the statement “dut_rpi2B_io = rpi2B_io(i_rpi2B,o_depp,o_rpi2B,to_depp)” in the file “my_wbdepp.py” in the toplevel.

The “i_depp” was set to 0x01, 0x00, 0x02, and 0x03. After setting the “i_depp” to 0x00 the signal “i_write_n” was set lo and then hi. The signal “x_write_n” is delayed by one clock. The signal “r_write_n is delay by 2 clocks.

The signal “i_astb_n” is set lo and then hi. The signal “x_astb_n” is delayed by one clock. The signal “r_astb_n is delay by 2 clocks.

The code that delays signals is working correctly.
Lines 112-115 and lines 188-201 of the file “toplevel.v”.
.
It appears that the code setting the “o_wait” is working currently. The signal goes lo following the signal “i_astb_n” going lo and the hi. This is in line 181 of the file “toplevel.v” assign o_wait = w_wait; which is dependent on line 185 assign w_wait = (!(x_dstb_n && x_astb_n && r_dstb_n && r_astb_n && l_dstb_n && l_astb_n));

Appendix A. my_wbdepp.py
Appendix B wbdeppsimple.v
Appendix C. toplevel.v