Co-Simultion
05/4/16

Steps needed for myhdl co-simulation

Note: The myhdl.vpi must be in the current directory.
The folder tb/vcd must be created.

Note1: Has been tested with iverilog
commit 1ea8a13bf877e6e74d52da5ce923876c8cc98764
Author: Stephen Williams <steve@icarus.com>
Date: Sat Feb 6 17:23:23 2016 -0800

Note2: Has been tested with MyHDL
commit 97dd4e3767082b31a18aecce763005ae374cf79d
Author: Jan Decaluwe <jan@jandecaluwe.com>
Date: Sun Oct 25 16:54:08 2015 +0100

“python dr_wbdepp.py –convert_rpi2B_io” which is used to create the file rpi2B_io.v

This file is Co-Simulated with the file tb/wbdeppsimple.v

To run the Co-Simulation

“python dr_wbdepp.py --cosimtrace”

To view the vcd file created by the Co-Simulation.

“gtkwave tb/vcd/wbdeppsimple1.vcd”

Ran a Python Co-Simulation i_rpi2B changes to_depp values which in turn changes i_depp.

The follow will be needed when adding memdev.v required 3 additional signals
i_wb_cyc, i_wb_stb, and i_wb_we.

This also required adding the following reg to the tb/tb_wbdeppsimple.v
        reg i_wb_cyc;
reg i_wb_stb;
reg i_wb_we;
In addition the instance of memdev was reguired
tb_memdev(i_clk, i_wb_cyc,
 i_wb_stb, i_wb_we, i_wb_addr,
 i_wb_data,o_wb_ack, o_wb_stall,
 o_wb_data);

The i_depp get sets.
The i_write_n goes lo.
The x_write_n is delayed by 1 clock from the i_write_n.
The r_write_n is delayed by 2 clock from the i_write_n.

The MSB bits 31:24 of the o_wb_addr chg on the falling
edge of l_dstb_n. The addr bits 2:0 need to be 000
and the dstb need to be hi on falling edge.

The MSB bits 23:16 of the o_wb_addr chg on the falling
edge of l_dstb_n. The addr bits 2:0 need to be 001
and the dstb need to be hi on falling edge.

The MSB bits 15:8 of the o_wb_addr chg on the falling
edge of l_dstb_n. The addr bits 2:0 need to be 010
and the dstb need to be hi on falling edge.

The MSB bits 7:0 of the o_wb_addr chg on the falling
edge of l_dstb_n. The addr bits 2:0 need to be 011
and the dstb need to be hi on falling edge.

As the values of i_depp are changed 0x01, 0x02, 0x03 and 0x04. o_wb_addr 0x01020304.

I set the address to 0xdeadbeef
address to 0xdeadbeef
Let's walk through an address write bus cycle:
1. The RPi waits until o_wait is zero, and hence the FPGA has stated that it is ready for a bus transaction.
2. The RPi sets the depp data values (I think you called these to_depp) and it sets write_n to zero
3. The RPi drops the address strobe line, i_astb_n.  The data strobe line *remains* *untouched*!
4. The FPGA raises the o_wait line to indicate an acknowledgement.
5. The RPi then raises the address strobe line, i_astb_n.  The data strobe line *remains* *untouched!

I chg 0xdeadbeef 0x00000000