05/2/16
Simulation.

/home/vidal/wkg/jpeg-2000-test/xula2_fpga/parallel/tb/wbdeppsimple.v
/home/vidal/wkg/jpeg-2000-test/xula2_fpga/parallel/wbdeppsimple/wbdeppsimple_tb.v

#103 i_int = 1;
      #104 i_write_n = 1;
#105 i_dstb_n = 1;
      #106 i_astb_n = 1;
#108 i_depp = 208;
#110 i_write_n = 0;
#112 i_astb_n = 0;
#113 i_dstb_n = 0;
      #114 i_write_n = 1;
#115 i_depp = 164;
      #116 i_astb_n = 1;
#117 i_dstb_n = 1;
      #118 i_write_n = 1;
#119 i_write_n = 0;
      #120 i_astb_n = 0;
      #121 i_dstb_n = 0;

      #123 i_astb_n = 1;
#124 i_dstb_n = 1;
      #126 i_write_n = 1;
      #128 i_astb_n = 0;
      #130 i_dstb_n = 0;
      #132 i_write_n = 0;
      #134 i_astb_n = 1;
      #136 i_dstb_n = 1;
      #138 i_write_n = 1;

end
      always i_clk = #5 ~i_clk; // 100 MHz
endmodule

Steps needed for myhdl co-simulation

Note: The myhdl.vpi must be in the current directory.
The folder tb/vcd must be created.

Note1: Has been tested with iverilog
commit 1ea8a13bf877e6e74d52da5ce923876c8cc98764
Author: Stephen Williams <steve@icarus.com>
Date: Sat Feb 6 17:23:23 2016 -0800

Note2: Has been tested with MyHDL
commit 97dd4e3767082b31a18aecce763005ae374cf79d
Author: Jan Decaluwe <jan@jandecaluwe.com>
Date: Sun Oct 25 16:54:08 2015 +0100

python dr_wbdepp.py –convert_rpi2B_io which is used to create the file rpi2B_io.v

python dr_wbdepp.py --cosimtrace

gtkwave tb/vcd/wbdeppsimple1.vcd

Ran a Python Co-Simulation toggled the i_b0 to i_b7 bits changes to_depp values.

Zooming in where the bits i_b0 to i_b7 drives to_depp. Here you see as bits i_b0 to i_b7 change the values of signal to_depp 0x02, 0x00, 0x04 ...0x88, 0x80, 0x00.

Zooming in where fr_depp drives from 0x00 to 0xff the bits o_b0 to o_b7.

As the values of i_depp are changed 0x00, 0x01, 0x02, and 0x03. o_wb_addr 0x00010203.