**********DRAFT**********
Testing C code with Ultibo Bare Metal, Ultibo TFTP and Ultibo Bitmaps
01/25/17
**********DRAFT**********

Goal: This is hopes of improving the speed of computing the JPEG 2000. The RPi2B or RPi3B will run Ultibo Bare Metal.
To transfer images over an Ethernet connection to a RPi2B or RPi3B.
Perform the JPEG 2000 lifting step which is the first step in the JPEG 2000.
The C code which which performs the Lifting step was develop by

Dan Gisselquist, Ph.D.
Gisselquist Technology, LLC

The C code that performs the DWT Lifting Step runs on x86_64 6 core is considerably faster.

time ./liftmain lena_rgb_512.png

real	0m0.090s
user	0m0.043s
sys	0m0.009s

The C code that performs the DWT Lifting Step runs on the x86_64 dual core and RPi3B is approximately the same.
On x86_64 dual core
time ./liftmain lena_rgb_512.png

real	0m0.356s
user	0m0.209s
sys	0m0.040s

On a RPi3B
./ltime ./liftmain lena_rgb_512.png

real	0m0.380s
user	0m0.230s
sys	0m0.010s

Status: Several Ultibo examples have been merged into a 4 program which displays a bitmap, calls a C library, and provides a TFTP server.

Processing time on Raspbian takes over 10 times more than Ultibo

./epochtime
time sec 1485366551
start time in sec 1485366551 end time in sec 1485366624 1e9 dwt processing time 73

This only takes 7 sec to perform the 1e9 dwt on Ultibo

Topleft is where the C routine is being called. Bottomleft is a 512 x 512 bitmap
In the file test.c the contents of lifing.c
In the topright is the tftp process.
# ultibo-tftp

A reasonably quick method of transferring files in an Ultibo project.
It uses Trival FTP based on RFC 1350

Approx upload times around 16 secs for kernel7.img of approx 2.2 MB

https://github.com/pjde/ultibo-tftp.git

tftp 192.168.1.185tftp> binary
tftp> put grn-out.32t aa
Sent 1048576 bytes in 5.0 seconds	1.67MBits/s
tftp> get aa bb
Received 1048580 bytes in 4.1 seconds	2.04MBits/s
tftp> quit

extern	void	singlelift(int rb, int w, int * const ibuf, int * const obuf);
extern	void	ilift(int rb, int w, int * const ibuf, int * const obuf);
extern	void	lifting(int w, int *ibuf, int *tmpbuf);

This is needed to add the fpc compiler to the PATH.

export PATH=/home/pi/ultibo/core/fpc/bin:$PATH
echo $PATH
/home/pi/ultibo/core/fpc/bin:/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin:/usr/local/games:/usr/games

arm-none-eabi-gcc -O2 -mabi=aapcs -marm -march=armv7-a -mfpu=vfpv3-d16 -mfloat-abi=hard -c test.c

arm-none-eabi-ar rcs libtest.a test.o

fpc -vi -B -Tultibo -Parm -CpARMV7A -WpRPI2B @/home/pi/ultibo/core/fpc/bin/rpi2.cfg -O2 LibCTestRPi2.lpr

./build_liftmain.sh compiles lifting.c & liftmain.c --> liftmain

iftmain lena_rgb_512.png
red-out.32t

line 101 lifting.c	const int	LVLS = 1; performs 1 level forward DWT

lines 230-246 in lifting.c when commented does not perform the inverse DWT.
/*
for(lvl=(LVLS-1); lvl>=0; lvl--) {
int	offset;

w <<= 1;

if (lvl)
offset = ov[lvl-1];
else
offset = 0;
ip = &ibuf[offset];
tp = &tmpbuf[offset];

ilift(rb, w, ip, tp);
ilift(rb, w, tp, ip);
}
*/

The image above is 1 level forward DWT red subband
The file red-out.32t

The image above is 3 levels forward DWT red subband
The file red-out.32t

The image above is 1 level forward DWT grn subband
The file grn-out.32t

The image above is 3 levels forward DWT grn subband
The file grn-out.32t

The image above is 1 level forward DWT blu subband
The file blu-out.32t

The image above is 3 levels forward DWT blu subband
The file blu-out.32t

The above image is the running on RPi3B as compiled for RPi2B on 01/23/17.