Comparing random values read from RPi2B UART to zipcpu at 1MBaud
06/09/16

Goal: To send RGB pixels extracted from file “/home/pi/jpeg-2000-test/jpeg2k/parallel_jpeg/lena_rgb_256.png”. Using the UART on a Raspberry Pi 2B and XuLA-LX2 FPGA running xulax25soc and StickIt-MB.

The image is 256 x 256 RGB.

The RGB data was extracted from the file from png file and written to “rgb.bin”.
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ uname -a
Linux raspberrypi2-146 4.4.11-v7+ #2 SMP Mon May 30 19:00:11 UTC 2016 armv7l GNU/Linux

pi@raspberrypi2-146:~ $ cd jpeg-2000-test/zipcpu/uart_test_code/
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ . setzipcpuPath.sh PATH,/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin:/usr/local/games:/usr/games:/home/pi/zipcpu/trunk/sw/install/cross-tools/bin:/home/pi/xulalx25soc/trunk/sw
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ make clean
rm -rf obj-zip/ h2
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ make
zip-gcc -O3 -Wall -Wextra -nostdlib -fno-builtin -c h2.c -o obj-zip/h2.o
h2.c: In function 'entry':
h2.c:48:9: warning: implicit declaration of function 'dwt_process' [-Wimplicit-function-declaration]
        dwt_process(buf_ptr);
        ^
h2.c:18:17: warning: unused variable 'my_results' [-Wunused-variable]
  struct results my_results;
        ^
zip-gcc -O3 -Wall -Wextra -nostdlib -fno-builtin -c pushtozipcpu.c -o obj-zip/pushtozipcpu.o
zip-gcc -O3 -Wall -Wextra -nostdlib -fno-builtin -c clr_sdram.c -o obj-zip/clr_sdram.o
zip-gcc -O3 -Wall -Wextra -nostdlib -fno-builtin -c dwt_steps.c -o obj-zip/dwt_steps.o
dwt_steps.c: In function 'dwt_steps':
dwt_steps.c:22:8: warning: variable 'h' set but not used [-Wunused-but-set-variable]
  int w,h;
        ^
dwt_steps.c:21:16: warning: unused variable 'dum3' [-Wunused-variable]
  int dum1,dum2,dum3;
        ^
dwt_steps.c:21:11: warning: unused variable 'dum2' [-Wunused-variable]
  int dum1,dum2,dum3;
        ^
dwt_steps.c:21:6: warning: unused variable 'dum1' [-Wunused-variable]
  int dum1,dum2,dum3;
      ^
dwt_steps.c:20:22: warning: variable 'dum7' set but not used [-Wunused-but-set-variable]
  int dum4,dum5,dum6,*dum7;
        ^
dwt_steps.c:20:16: warning: variable 'dum6' set but not used [-Wunused-but-set-variable]
  int dum4,dum5,dum6,*dum7;
        ^
dwt_steps.c:19:50: warning: variable 'dum3_b' set but not used [-Wunused-but-set-variable]
  int dum2_r,dum2_g, dum2_b,dum2_l,dum3_r,dum3_g, dum3_b,dum3_l;
        ^
dwt_steps.c:19:21: warning: variable 'dum2_b' set but not used [-Wunused-but-set-variable]
  int dum2_r,dum2_g, dum2_b,dum2_l,dum3_r,dum3_g, dum3_b,dum3_l;
        ^
dwt_steps.c:18:29: warning: variable 'dum1_b' set but not used [-Wunused-but-set-variable]
  int col,row,dum1_r,dum1_g, dum1_b,dum1_l;
        ^
dwt_steps.c:18:21: warning: variable 'dum1_g' set but not used [-Wunused-but-set-variable]
  int col,row,dum1_r,dum1_g, dum1_b,dum1_l;
        ^
dwt_steps.c:18:10: warning: unused variable 'row' [-Wunused-variable]
  int col,row,dum1_r,dum1_g, dum1_b,dum1_l;
        ^
dwt_steps.c:15:7: warning: unused variable 'array_ptr' [-Wunused-variable]
  int *array_ptr;
       ^
dwt_steps.c:11:15: warning: unused variable 'LED_OFF_DWT' [-Wunused-variable]
     const int LED_OFF_DWT = 0x10000;
        ^
zip-gcc -O3 -Wall -Wextra -nostdlib -fno-builtin -c dwt_process.c -o obj-zip/dwt_process.o
dwt_process.c: In function 'dwt_process':
dwt_process.c:14:5: warning: value computed is not used [-Wunused-value]
     *imgbuf++;
     ^
dwt_process.c:17:5: warning: value computed is not used [-Wunused-value]
     *imgbuf++;
     ^
dwt_process.c:19:2: warning: value computed is not used [-Wunused-value]
  *imgbuf++;
  ^
dwt_process.c:23:3: warning: value computed is not used [-Wunused-value]
   *imgbuf--;
   ^
dwt_process.c:7:15: warning: unused variable 'rr' [-Wunused-variable]
     const int rr = 0xff00000;
        ^
dwt_process.c:3:15: warning: unused variable 'LED_ON_DWT' [-Wunused-variable]
     const int LED_ON_DWT = 0x10001;
        ^
zip-gcc -T xula.ld -Wl,-Map,obj-zip/h2.map obj-zip/h2.o obj-zip/pushtozipcpu.o obj-zip/clr_sdram.o obj-zip/dwt_steps.o obj-zip/dwt_process.o -o h2

Note: In order to detect the toggle of gpio from zipcpu PIGPIO is used.
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ sudo pigpiod

pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ ./ldfpga
Success: Bitstream in /home/pi/toplevel.bit downloaded to FPGA on XuLA2-LX9!

pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ ./stzipcpu.sh
Halting the CPU
Clearing the cache
The CPU should be fully loaded, you may now start
it. To start the CPU, type wbregs cpu 0
signal from zipcpu 0
waiting for hello, world!
signal from zipcpu 1
sending data
transfer time 1.93587684631 sec
waiting for Data rdy !
Hello,

Random values were checked it appears that all values are correct.

pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs cpu 0
01000000 ( ZIPCTRL)-> 00000000
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80ffff
0080ffff ( no name) : [.q$Q] 0b712451
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80ffff
0080ffff ( no name) : [.q$Q] 0b712451
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x800000
00800000 ( SDRAM) : [."$|] 0e22247c
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x805d8e
00805d8e ( no name) : [....] 0cc2a09d
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x808e80
00808e80 ( no name) : [....] 0e120085
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80ac3e
0080ac3e ( no name) : [...j] 06e0d86a
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80d3e5
0080d3e5 ( no name) : [.S0.] 0f533095
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80e8f6
0080e8f6 ( no name) : [.!.X] 09210858
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80f9b0
0080f9b0 ( no name) : [."..] 0e22c0a3
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80fffe
0080fffe ( no name) : [.!.L] 0b210c4c
pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs 0x80ffff
0080ffff ( no name) : [.q$Q] 0b712451