Building the xulalx25soc & zipcpu for XulA2-LX9
for the RPi2B & Ubuntu

C compiler for zipcpu

06/12/16 build Ver 83 xulalx25soc & Ver 152 zipcpu

The xula.ucf was configured to match the RPi2B to provide a hi-speed data transfer between the zipcpu and the RPi2B. Current tests indicate that 1MBaud can transferred 256 x 256 RGB pixel to the zipcpu in 1.93375396729 sec. In addition the GPIO from the zipcpu can be used to handshake between the RPi2B and the zipcpu. This provides visual and signals to start the data transfer from the RPi2B to the zipcpu. For additional information see the compare_results.odt document.
The results of testing communication between the RPi2B and zipcpu are found “compare_results.odt”

On Ubuntu build of zipcpu needed to copy zasm.tab.c & zasm.tab.h to zipcpu/trunk/sw/zasm/obj-pc
since it has older version of bison.
vidal@ws009:~/wkg/zipcpu/trunk/sw$ ls install/cross-tools/bin/
zasm zip-c++filt zip-gcc-ar zip-gprof zip-ranlib
zdump zip-cpp zip-gcc-nm zip-ld zip-readelf
zip-addr2line zip-elfedit zip-gcc-ranlib zip-ld.bfd zip-size
zip-ar zip-g++ zip-gcov zip-nm zip-strings
zip-as zip-gcc zip-gcov-tool zip-objcopy zip-strip
zip-c++ zip-gcc-5.3.0 zip-gfortran zip-objdump zpp

The current projects xulalx25soc & zipcpu are managed in subversion at opencores.org.

 cd wkg

mkdir -p svn/uart_rpi_xulalx25soc/xulalx25soc

cd ssvn/uart_rpi_xulalx25soc/xulalx25soc

svn co --username yyyyyyy --password xxxxxxxx http://opencores.org/ocsvn/xulalx25soc/xulalx25soc/trunk

vidal@ws009:~/wkg/svn/uart_rpi_xulalx25soc/xulalx25soc/trunk$ svn info
Path: .
URL: http://opencores.org/ocsvn/xulalx25soc/xulalx25soc/trunk
Repository Root: http://opencores.org/ocsvn/xulalx25soc
Repository UUID: 6dd62048-26e6-457e-a111-74efc207c9ac
Revision: 83
Node Kind: directory
Schedule: normal
Last Changed Author: dgisselq
Last Changed Rev: 83
Last Changed Date: 2016-06-09 15:04:41 -0600 (Thu, 09 Jun 2016)

cd wkg

mkdir -p svn/uart_rpi_xulalx25soc/zipcpu

svn co --username yyyyyyy --password xxxxxxxx http://opencores.org/ocsvn/zipcpu/zipcpu/trunk
/home/vidal/wkg/svn/zipcpu/trunk

vidal@ws009:~/wkg/svn/uart_rpi_xulalx25soc/zipcpu/trunk$
Path: .
URL: http://opencores.org/ocsvn/zipcpu/zipcpu/trunk
Repository Root: http://opencores.org/ocsvn/zipcpu
Repository UUID: 753a1494-afa9-4eb1-9a3f-b6aaa4ffd0d3
Revision: 152
Node Kind: directory
Schedule: normal
Last Changed Author: dgisselq
Last Changed Rev: 152
Last Changed Date: 2016-05-12 20:05:54 -0600 (Thu, 12 May 2016)

Create a svn repository on Ubuntu at /home/vidal/wkg/svn/uart_rpi_xulalx25soc

A Description of Xulalx25soc from opencores is found at Appendix A.

A Description of ZipCpu is found at Appendix B.

The original xulalx25soc supported the XulA2-LX25. Now the project supports both the XulA2-LX9 & XulA2-LX25. In addition the binutils-2.25 & gcc-5.3.0 for the zipcpu are provided.

Features of XulA2 models found at Appendix C. XulA2-LX25 & XulA2-LX9 freatures.

Software in home/vidal/wkg/svn/uart_rpi_xulalx25soc/xulalx25soc/trunk/rtl is what is used to create the bit file.

Details of bit file creation are found at Appendix D. Bit file generation.
vidal@ws009:~/wkg/svn/test_xula2soc$ ls -la toplevel.bit
-rw-rw-r-- 1 vidal vidal 341253 Apr 21 21:22 toplevel.bit
e96c88ed26e5b02039477a63201ed91b toplevel.bit
The toplevel.bit needs to transferred to RPi2B. The location on the RPi2B is
/home/pi/tmp_svn_bld_bitfiles/toplevel.bit

Creating the software to communicate with the FPGA is found at Appendix E. RPi2B Software.

The zip-objdump -d h2 is found at Appendix F. The zip-objdump -d h2

Details of software build are found at Appendix G Ubuntu zipcu & xulalx25soc software build.

Testing xulalx25soc found at Appendix H Ubuntu test

Details of zipcpu are found at Appendix I Notes on Update to zipcpu rev152.

A test was run testing the RPi2B writing to SDRAM found at Appendix I. SDRAM test.
The data was created from the image lena_256.png with the python file jpeg-2000-test/pc_fast_blinker_jpeg/input_examples$ ls xula2_dum.py. This creates 32 bit values of 3 pixels and the flgs.
2 0xa4 0xa4 0xa4
2 982599844 0x3a9148a4
4 0xa4 0x9c 0x9c
4 982595740 0x3a91389c
6 0x9c 0x9c 0xa4
6 980498596 0x3a7138a4
.
.
.
246 0x2c 0x2c 0x34
246 951081012 0x38b05834
248 0x34 0x34 0x34
248 953182260 0x38d06834
250 0x34 0x34 0x34
250 953182260 0x38d06834
252 0x34 0x34 0x34
252 953182260 0x38d06834
Appendix A. Description of Xulalx25soc from opencores
## Description
This project attempts to take two separate projects, the OpenCores ZipCPU and Xess.com's XuLA2-LX25, and merge them together into a single System on a Chip implementation. As currently envisioned, this implementation will offer the following peripherals to the ZipCPU within:
- External Peripherals
  - 14 GPIO inputs, 15 GPIO outputs
  - PWM output
  - Rx and Tx UART ports
  - 1MB SPI Flash, together with a read/write controller
  - 32MB SDRAM
  - (SD-Card --- controller not yet built)
- Internal Peripherals
  - Real-time clock and date
  - Access to the FPGA configuration port, for unattended updates
  - Zip CPU debug/configuration port access from JTAG
- Zip CPU Peripherals
  - 3x timers, each of which can be programmed either in a one shot mode or as a repeating interval timer
  - A watchdog timer, and a Wishbone bus watchdog timer
  - Two interrupt controllers
  - Direct Memory Access (DMA) Controller for unattended memory movement
## Current Status
Although the project was only created in December, 2015, it is already fully featured. Most of the components have been pulled from other projects, either here on open cores or from within our personal vault. What remains is to complete the documentation describing the various components, to determine that these pieces can be built successfully from their SVN repository, and whether or not the peripheral list is sufficient for the project needs.
## Unique Features
This System on a Chip controller has some unique features associated with it, above and beyond the peripherals listed above. Primary among those is the JTAG (or even UART) to 32-bit wishbone master conversion. This makes it possible for an external entity to read from or write to the wishbone bus. Uses include verifying whether or not peripherals work, as well as configuring the CPU, memory and flash for whatever purpose one might have. This particular capability was designed so that FPGA control programs can call a common set of bus interface functions to communicate with the FPGA, regardless of how the bus was actually implemented.
A second unique feature is a PWM driver that spreads its digital energy into higher (non-auditory) frequencies which can then be filtered out easier with a simple low-pass filter. As an example, sending a zero, or half pulse width, will result in alternating digital ones and zeros from the driver. While I expect this will have a pleasing effect on the ear, especially since these transitions will be outside of normal hearing range, this is the first time I have tried it and the jury's still out regarding whether or not it works or even works well.
Finally, while it may not really be that unique, this core does feature a fully functional SDRAM controller capable of one read cycle (or write cycle) every two clocks when pipelined. Unlike many other dynamic memory controllers, this one was not created from a proprietary, closed source, memory interface generation facility.
Appendix B. Description of ZipCpu
## Description
The original goal of the ZIP CPU was to be a very simple CPU. You might think of it as a poor man's alternative to the OpenRISC architecture. For this reason, all instructions have been designed to be as simple as possible, they all work on 32--bit operands, and all of the ALU instructions are designed to be executed in one instruction cycle per instruction, barring pipeline stalls. This has resulted in the choice to drop push and pop instructions, pre-increment and post-decrement addressing modes, and more.
In bare bullet form, the Zip CPU is:
- A 32-bit CPU: All registers are 32-bits, addresses are 32-bits, instructions are 32-bits wide, etc.
- A RISC CPU. There is no microcode for executing instructions.
- A Load/Store architecture. (Only load and store instructions can access memory.)
- Wishbone compliant. All peripherals are accessed just like memory across this bus.
- A Von-Neumann architecture. (The instructions and data share a common bus.)
- A pipelined architecture, having stages for Prefetch, Decode, Read-Operand, Execute, and Write-back. The Execute stage is implemented by one of four blocks: an arithmetic/logic unit, a memory unit, a divide coprocessor and a floating point coprocessor (once completed). The last two blocks, the divide and floating point, will always be optional. There inclusion will be chosen based upon your implementation needs.
## Current Status
The Zip CPU and Zasm assembler currently pass all of our in house testing. They are ready for bigger projects. All of the peripherals, save the DMA, are in good working order. (The DMA hasn't yet been tested ... let me know if you have a good test case to try it on.)
The Zip CPU has been tested and proven itself by processing a GPS NMEA stream from a Digilent GPS module connected to a Basys-3 development board. Further development is taking place here.
Our next task with this CPU will be to build both a compiler and a small embedded operating system. I intend to test the compiler, and indeed the CPU itself, on the Dhrystone benchmark as a first test. Beyond that, we are currently working on a market analysis and survey before diving full bore into either of these tasks. My hope is that I might be able to demonstrate a new concept in embedded Operating System design through this process, but I have yet to determine or decide what that new concept might be.
20151222 Update: We have just finished testing a new, albeit similar, instruction set, and an entirely rebuilt prefetch/cache. The new instruction set has two specific new features. The first new feature is a 5-bit opcode, rather than the 4-bit opcode from before. This 5-bit opcode offers room for divide and floating point instructions which the CPU didn't have before. (I even threw in instructions in for bit reversal and pop count ... since I had two new ALU opcodes to use.) A divide implementation has also been built, integrated, and tested. The divide fits, like the floating point unit will, next to the ALU/Memory units in the same pipeline stage, but parallel to the other units. In all other respects, the new instruction set is compatible at the assembly level with the previous instruction set--although support for immediates has lost 1-2 bits in the process depending upon the instruction. The second new feature is the ability to compress two instructions into a single 32-bit instruction word. This feature, while implemented in the ZipCPU, has not yet been integrated into the toolset, so it has not been thoroughly tested yet. The bigger news is the new cache. This new cache can roughly double the performance of the CPU while running Dhrystone. This cache, though, can drastically increase the number of memory LUT's used by the ZipCPU, so its inclusion is optional--depending upon a compile time definition.
## Performance
I have a couple of performance measures to offer at this time. The first is that, in practice, this CPU can execute 0.4 instructions per clock in its test set. Of course, this is somewhat dependent upon the code that the CPU is executing, so your mileage may vary. Were it not for pipeline stalls, the Zip CPU would be able to handle one instruction per clock. As a second performance measure, the Zip CPU fits within 2,800 6-input LUTs on an Artix-7 (today's build was at 2,796), and the full Zip System within 3,400 LUTs (today's build was at 3,315). Of course, you might not find yourself needing all of these LUTs. The ZipSystem and CPU also have build-time defines which can be used to drop this LUT count down to 1,040 for the ZipBones system (including CPU), so don't let the 3,400 LUT count scare you. As a third reference point, I am running it on a Basys-3 board hosting an Artix-7(35T) running at a 100 MHz clock, and on a XuLA2-LX25 board with an 80 MHz clock. A build has also been developed for a Cmod-S6 board that will run with an 80 MHz clock as well. Hopefully these measures are good enough for you. If not, why not build it and try it yourself?
## Packaged flavors

As created, the Zip CPU has no peripherals. It is simply a set of pipeline stages implementing a CPU. Options exist to remove much of the pipeline logic, the divide or floating point units, which put together can either make the CPU fit in very small places, or equivalently make the CPU very fast, all dependent upon your needs.

Because the CPU alone is so very bare, the Zip CPU ships with a minimalist set of peripherals, which when put together become the Zip System. Still, the ZipSystem is not designed to be a System on a Chip (SoC), but rather a System within a Chip (SwiC). Thus, should you wish to make a complete system from the ZipSystem, you will probably still wish to add other peripherals such as a UART, clock, memory controller, or more (not included). While these might be included with the ZipCPU, we expect that you will wish to tailor your CPU to your environment, especially if you are looking for a small and simple CPU.

Some users, such as those trying to keep and maintain a minimal FPGA footprint, may not wish to have all of the extra baggage found in the Zip System. Perhaps they only wish to have some (or none) of these peripherals, and wish to handle the bus interconnect themselves. For these interested parties a bare version of just the Zip Bones is available. We have used this approach successfully to place the Zip CPU into some very small FPGA's. / Of course, given the RTL availability under the GPL, you are more than welcome to build and try out your own interface to the Zip CPU if you so choose!

## Why build a custom CPU?
Many people have asked me why I am building the Zip CPU. ARM processors are good and effective. Xilinx makes and markets Microblaze, Altera Nios, and both have better toolsets than the Zip CPU will ever have. OpenRISC is also available, RISC-V is arguably better and may be replacing it. Why build a new processor?
The easiest, most obvious answer is the simple one: Because I can.
There's more to it, though. There's a lot that I would like to do with a processor, and I want to be able to do it in a vendor independent fashion. I would like to be able to generate Verilog code that can run equivalently on both Xilinx and Altera chips, and that can be easily ported from one manufacturer's chipsets to another. Even more, before purchasing a chip or a board, I would like to know that my soft core works. I would like to build a test bench to test components with, and Verilator is my chosen test bench. This forces me to use all Verilog, and it prevents me from using any proprietary cores. For this reason, Microblaze and Nios are out of the question.
Why not OpenRISC? That's a hard question. The OpenRISC team has done some wonderful work on an amazing processor, and I'll have to admit that I am envious of what they've accomplished. I would like to port binutils to the Zip CPU, as I would like to port GCC and GDB. They are way ahead of me. The OpenRISC processor, however, is complex and hefty at about 4,500 LUTs. It has a lot of features of modern CPUs within it that ... well, let's just say it's not the little guy on the block. The Zip CPU is lighter weight, costing only about 2,300 LUTs with no peripherals, and 3,200 LUTs with some very basic peripherals.
My final reason is that I'm building the Zip CPU as a learning experience. The Zip CPU has allowed me to learn a lot about how CPUs work on a very micro level. For the first time, I am beginning to understand many of the Computer Architecture lessons from years ago. Better still, and thanks to Dr. Sauerman's wonderful Embedded Operating System Book, I may even choose to apply these concepts towards building my own Operating System.
To summarize: Because I can, because it is open source, because it is light weight, and as an exercise in learning.
## Not so Simple
Now, however, that I've worked on the Zip CPU for a while, it is not nearly as simple as I originally hoped. Worse, I've had to adjust to create capabilities that I was never expecting to need. These include:
- External Debug: Once placed upon an FPGA, I'm going to need a means of debugging this CPU. That means that there needs to be an external register that can control the CPU: reset it, halt it, step it, and tell whether it is running or not. Another register is placed similar to this register, to allow the external controller to examine registers internal to the CPU.
- Internal Debug: Being able to run a debugger from within a user process requires an ability to step a user process from within a debugger. It also requires a break instruction that can be substituted for any other instruction, and substituted back. The break is actually difficult: the break instruction cannot be allowed to execute. That way, upon a break, the debugger should be able to jump back into the user process to step the instruction that would've been at the break point initially, and then to replace the break after passing it.
- Prefetch Cache: My original implementation had a very simple prefetch stage. Any time the PC changed the prefetch would go and fetch the new instruction. While this was perhaps this simplest approach, it cost roughly five clocks for every instruction. This was deemed unacceptable, as I wanted a CPU that could execute instructions in one cycle. I therefore have a prefetch cache that issues pipelined wishbone accesses to memory and then pushes instructions at the CPU. Sadly, this accounts for about 20% of the logic in the entire CPU, or 15% of the logic in the entire system. On a brighter note, when coupled with the Quad SPI Flash wishbone controller, this CPU can execute code directly from a flash device, although fetches from such a device may require more than 16 clocks per instruction.
- Operating System: In order to support an operating system, interrupts and so forth, the CPU needs to support supervisor and user modes, as well as a means of switching between them. For example, the user needs a means of executing a system call. This is the purpose of the 'trap' instruction. This instruction needs to place the CPU into supervisor mode (here equivalent to disabling interrupts), as well as handing it a parameter such as identifying which O/S function was called.
  My initial approach to building a trap instruction was to create an external peripheral which, when written to, would generate an interrupt and could return the last value written to it. This failed timing requirements, however: the CPU executed two instructions while waiting for the trap interrupt to take place. Since then, I've decided that any request from user mode to switch to supervisor mode (i.e., clearing the Global Interrupt Enable (GIE) bit in the CC register, will also set a trap bit in the CC register. Once in supervisor state, the supervisor may then check a trap bit within the CC register to know that it got there from a user mode "trap" instruction. (i.e., user mode cleared the GIE bit) As for which trap was executed, that can easily be handled by the value of R0 at the time the trap was called. (Any other register could work just as well, the choice of R0 is arbitrary.
  Modern timesharing systems also depend upon a Timer interrupt to handle task swapping. For the Zip CPU, this interrupt is handled external to the CPU as part of the CPU System, found in zipsystem.v. The timer module itself is found in ziptimer.v.
- Pipeline Stalls: My original plan was to not support pipeline stalls at all, but rather to require the compiler to properly schedule instructions so that stalls would never be necessary. After trying to build such an architecture, I gave up, having learned some things:
  For example, in order to facilitate interrupt handling and debug stepping, the CPU needs to know what instructions have finished, and which have not. In other words, it needs to know where it can restart the pipeline from. Once restarted, it must act as though it had never stopped. This killed my idea of delayed branching, since what would be the appropriate program counter to restart from following an interrupt? The instruction the CPU was going to branch to, or the instruction(s) in the delay slots?
  So I switched to a model of discrete execution: Once an instruction enters into either the ALU or memory unit, the instruction is guaranteed to complete. If the logic recognizes a branch or a condition that would render the instruction entering into this stage possibly inappropriate (i.e. a conditional branch preceeding a store instruction for example), then the pipeline stalls for one cycle until the conditional branch completes. Then, if it generates a new PC address, the stages preceeding are all wiped clean.
  This was later modified, so that if an instruction enters the memory unit it is then guaranteed to complete, while instructions may go through the ALU only to have its write back stage disabled. This change reduced the number of pipeline stalls, such as the stalls for a conditional branch not taken.
  The discrete execution model allows such things as sleeping: if the CPU is put to "sleep", the ALU and memory stages stall and back up everything before them. Likewise, anything that has entered the ALU or memory stage when the CPU is placed to sleep continues to completion. For this reason, the ALU/MEM stages will introduce a stall cycle after any write to the CC register (not after an instruction modifying flags), so that the sleep instruction will halt at the sleep instruction.
  To handle this logic, each pipeline stage has three control signals: a valid signal, a stall signal, and a clock enable signal. In general, a stage stalls if it's contents are valid and the next step is stalled. This allows the pipeline to fill any time a later stage stalls.
- Verilog Modules: When examining how other processors worked here on open cores, many of them had one separate module per pipeline stage. While this appeared to me to be a fascinating and commendable idea, my own implementation didn't work out quite so nicely.
  As an example, the decode module produces a lot of control wires and registers. Creating a module out of this, with only the simplest of logic within it, seemed to be more a lesson in passing wires around, rather than encapsulating logic.
  Another example was the register writeback section. I would love this section to be a module in its own right, and many have made them such. However, other modules depend upon writeback results other than just what's placed in the register (i.e., the control wires). For these reasons, I didn't manage to fit this section into it's own module.

Appendix C. XulA2-LX25 & XulA2-LX9 freatures.
LX25

LX9

LX25

- Open-source design
- XC6SLX25 FPGA
- 32 MByte SDRAM
- 8 Mbit Flash
- microSD card socket
- 3.3 & 1.2V regulators
- 40-pin interface
- 12 MHz oscillator
- PIC 18F14K50 micro
- USB 2.0 port
- Auxiliary JTAG port
- Works with the XSTOOLs software
- Works with XILINX ISE and WebPACK
- Works with XILINX iMPACT and ChipScope (requires Xilinx JTAG cable)

LX9

- Open-source design
- XC6SLX9 FPGA
- 32 MByte SDRAM
- 8 Mbit Flash
- microSD card socket
- 3.3 & 1.2V regulators
- 40-pin interface
- 12 MHz oscillator
- PIC 18F14K50 micro
- USB 2.0 port
- Auxiliary JTAG port
- Works with the XSTOOLs software
- Works with XILINX ISE and WebPACK
- Works with XILINX iMPACT and ChipScope (requires Xilinx JTAG cable)
Appendix D. Bit file generation.

Different toplevel.bit files can be created depending if the line 1 in the file busmaster.v & line 1 in file
cpudefs.v
// `define	XULA25. If the line is uncomented the toplevel.bit will be built for XulA2-LX25.

The xulalx25soc provides the Verilog files to create the toplevel.bit file using the Xilinx WebPack.

cd ~/wkg/svn/uart_rpi_xulalx25soc/xulalx25soc/trunk$

make datestamp to create the file 20160609-build.v

`define DATESTAMP 32'h20160609

This will be used with the after the toplevel.bit is installed on the XulA2-LX9 FPGA .

pi@raspberrypi2-146:~/jpeg-2000-test/zipcpu/uart_test_code $ wbregs version
00000101 ( VERSION) : [....] 20160609

. /opt/Xilinx/14.6/ISE_DS/settings64.sh

ise

Create a new project.

Depress Next

On the next screen is where you need to select XC6SLX9 XC6SLX25.

Depress Next.

Depress Finish
Need to add the sources for Verilog files and the User constraints.

Depress Open

Adding Source Files will appear.

Depress OK

Next CPU files need to be added .

Depress Open

Adding Source Files will appear.

Depress OK

Next need to add the constraints file.

Depress Open
Adding Source Files will appear.

Depress OK

Now hight the Generate Programming File
Right Click Depress Run

The result is that the majority of the CPU code can be found in the zipcpu.v file.

On an AMD 6 core running Ubuntu 12.04 this takes approximatly 6 mins.

Process "Generate Programming File" completed successfully

vidal@ws009:~/wkg/svn/uart_rpi_xulalx25soc/uart_rpi2B$ ls -la toplevel.bit
-rw-rw-r-- 1 vidal vidal 341253 Jun 9 18:13 toplevel.bit
fa32e8ede6909b714919e0578da74b58 toplevel.bit

Number of Slice LUTs	5,273	5,720	92%
Number used as logic	5,056	5,720	88%

Memory

Number used as Memory	198	1,440	13%

16bit

Number of RAMB16BWERs	20	32	62%

8bit

Number of RAMB8BWERs	3	64	4%

DCM

Number used as DCMs	2

IOBs

Number of LOCed IOBs	78	78	100%

Appendix E. RPi2B Software

What's in zipcpu: A cpu and it's support only.  Within the subdirectories ...
rtl ... A set of .v files used to implement the CPU.  These files also exist in the xula project.  Their purpose in the zipcpu project is to build a Verilator testbench to prove that the CPU works.
bench/cpp ... The verilator testbench, zippy_tb, used to prove that the CPU works.
bench/asm ... Several assembly files used with the test bench, also to prove that the CPU works.
sw/zasm ... The assembler you are no longer using.
doc/ ... Documents which come with the repository, that you do not need to build
The dependencies between this and the XuLA SoC are: binutils (zip-as, zip-ld, zip-objdump, zip-readelf, etc.), GCC (zip-gcc, zip-cc, zip-cc1, zip-cpp, etc.), and the source code for disassembling instructions for the debugger in xula../trunk/sw/zipdbg.
This is what I see chg'ed in zipcpu  -r 108
-all: doc rtl sw bench
+all: rtl
I am trying to understand what is required, between zipcpu & xulalx25soc.
It appears that in zipcpu/trunk/sw binutils & gcc should be built with scripts not makefiles
Are these dependent on zipcpu/trunk/rtl?
How about zipcpu/trunk/sw/zasm? I make before  binutils & gcc.

 Only zipcpu/trunk/rtl which uses a Makefile

The xulalx25soc is dependent on zipcpu is that correct?

Where is the simulator and which requires a XulA2 connected?

A copy of svn/xulalx25soc/ & svn/zipcpu is required on the RPi2B.

zipcpu/trunk
Revision: 152
Last Changed Date: 2016-03-15 13:55:36 +0000 (Tue, 15 Mar 2016)

xulalx25soc/trunk
Revision: 83
Last Changed Date: 2016-03-14 21:43:20 +0000 (Mon, 14 Mar 2016)

pi@raspberrypi2-146 cp -R svn/xulalx25soc/ .
pi@raspberrypi2-146 cp -R svn/zipcpu/ .

pi@raspberrypi2-146 cd zipcpu/trunk/

pi@raspberrypi2-146 make

pi@raspberrypi2-145 ~ $ ls zipcpu/trunk/rtl/obj_dir/
Vdiv__ALL.a Vzipbones__ALL.a Vzipsystem__ALL.a
Vdiv__ALLcls.cpp Vzipbones__ALLcls.cpp Vzipsystem__ALLcls.cpp
Vdiv__ALLcls.d Vzipbones__ALLcls.d Vzipsystem__ALLcls.d
Vdiv__ALLcls.o Vzipbones__ALLcls.o Vzipsystem__ALLcls.o
Vdiv__ALLsup.cpp Vzipbones__ALLsup.cpp Vzipsystem__ALLsup.cpp
Vdiv__ALLsup.d Vzipbones__ALLsup.d Vzipsystem__ALLsup.d
Vdiv__ALLsup.o Vzipbones__ALLsup.o Vzipsystem__ALLsup.o
Vdiv_classes.mk Vzipbones_classes.mk Vzipsystem_classes.mk
Vdiv.cpp Vzipbones.cpp Vzipsystem.cpp
Vdiv.h Vzipbones.h Vzipsystem.h
Vdiv.mk Vzipbones.mk Vzipsystem.mk
Vdiv__Syms.cpp Vzipbones__Syms.cpp Vzipsystem__Syms.cpp
Vdiv__Syms.h Vzipbones__Syms.h Vzipsystem__Syms.h
Vdiv__ver.d Vzipbones__ver.d Vzipsystem__ver.d
Vdiv__verFiles.dat Vzipbones__verFiles.dat Vzipsystem__verFiles.dat

pi@raspberrypi2-145 ~ $ cd zipcpu/trunk/sw/zasm/

make

pi@raspberrypi2-145 ~/zipcpu/trunk/sw/zasm $ ls
asmdata.cpp optest test.S zasm.l zopcodes.cpp zpp
asmdata.h optest.cpp twoc.cpp zasm.y zopcodes.h zpp.l
Makefile sys.i twoc.h zdump zparser.cpp
obj-pc tags zasm zdump.cpp zparser.h

cd sw

make

If/when you need to build a new binutils, ...
cd zipcpu/trunk/sw
rm -rf build-gas binutils-2.25/
bash gas-script.sh
The same is true with GCC.  If/when you need to build a new GCC ...
cd zipcpu/trunk/sw
rm -rf build-gcc gcc-5.3.0-zip/
bash gcc-script.sh
pi@raspberrypi2-146 ~/zipcpu/trunk/sw $ bash gas-script.sh
pi@raspberrypi2-146 ~/zipcpu/trunk/sw $ bash gcc-script.sh

Note: Software in the zipcpu/trunk/sw must be built before the
xulalx25soc/trunk/sw

 cd ~/xulalx25soc/trunk/sw/

 cp ~/zipcpu/trunk/sw/zasm/zopcodes.h .
 cp ~/zipcpu/trunk/sw/zasm/zparser.h .

Note : Modfified the ~/xulalx25soc/trunk/sw/ Makefile
 diff -u Makefile ~/svn/xulalx25soc/trunk/sw/Makefile
--- Makefile	2016-03-15 17:20:29.093265544 +0000
+++ /home/pi/svn/xulalx25soc/trunk/sw/Makefile	2016-03-11 23:41:39.338808462 +0000
@@ -39,8 +39,7 @@
 LIBUSBINC := -I/usr/include/libusb-1.0/
 LIBUSBDIR := -L/usr/lib/x86_64-linux-gnu
 OBJDIR := obj-pc
-#ZIPD := /home/dan/work/rnd/zipcpu/trunk/sw/zasm
-ZIPD := /home/pi/zipcpu/trunk/sw/zasm
+ZIPD := /home/dan/work/rnd/zipcpu/trunk/sw/zasm
 BUSSRCS := ttybus.cpp llcomms.cpp regdefs.cpp usbi.cpp
 SOURCES := ziprun.cpp zipdbg.cpp dumpsdram.cpp wbregs.cpp netusb.cpp	\
 flashdrvr.cpp $(BUSSRCS)

#ZIPD := /home/dan/work/rnd/zipcpu/trunk/sw/zasm
ZIPD := /home/pi/zipcpu/trunk/sw/zasm

make clean

make

pi@raspberrypi2-146 ~/xulalx25soc/trunk/sw $ ./wbregs version
00000101 ( VERSION) : [....] 2016031

Old below this line***************************************************
mkdir -p svn/xulalx25soc
mkdir -p svn/zipcpu
cd svn/xulalx25soc
svn co --username yyyyyyy --password xxxxxxxx http://opencores.org/ocsvn/xulalx25soc/xulalx25soc/trunk

/home/pi/svn/xulalx25soc/trunk
Revision: 34
Last Changed Date: 2016-03-11 01:05:38 +0000 (Fri, 11 Mar 2016)

cd svn/zipcpu
svn co --username yyyyyyy --password xxxxxxxx http://opencores.org/ocsvn/zipcpu/zipcpu/trunk
/home/pi/svn/zipcpu/trunk
Revision: 105
Last Changed Date: 2016-03-09 15:26:16 +0000 (Wed, 09 Mar 2016)

cd ~/

cp -R svn/xulalx25soc/ .

cp -R svn/zipcpu/ .

Note: Software in the zipcpu/trunk/sw must be built before the
xulalx25soc/trunk/sw

The Makefile in the zipcpu/trunk still is producing errors.
pi@raspberrypi2-145 ~/zipcpu/trunk $ make
Building docs
make[2]: *** No targets specified and no makefile found. Stop.
Makefile:13: recipe for target 'pdftex' failed
make[1]: *** [pdftex] Error 2
Makefile:52: recipe for target 'doc' failed
make: *** [doc] Error 2

cd zipcpu/trunk/rtl
make
This creates the obj_dir
There are 3 files that are in the obj_dir that require modifications.
VERILATOR_ROOT = /home/pi/share/verilator → VERILATOR_ROOT = /usr/local/share/verilator

Vzipsystem.mk
Vzipbones.mk
Vdiv.mk
Note: Dan I think you made a chg in one of the upper level Makefiles based on when I was using verilator installed in /home/pi. Verilator is installed in /usr/local/.

pi@raspberrypi2-149 ~/zipcpu/trunk/rtl $ ls obj_dir/
Vdiv__ALL.a Vzipbones__ALL.a Vzipsystem__ALL.a
Vdiv__ALLcls.cpp Vzipbones__ALLcls.cpp Vzipsystem__ALLcls.cpp
Vdiv__ALLcls.d Vzipbones__ALLcls.d Vzipsystem__ALLcls.d
Vdiv__ALLcls.o Vzipbones__ALLcls.o Vzipsystem__ALLcls.o
Vdiv__ALLsup.cpp Vzipbones__ALLsup.cpp Vzipsystem__ALLsup.cpp
Vdiv__ALLsup.d Vzipbones__ALLsup.d Vzipsystem__ALLsup.d
Vdiv__ALLsup.o Vzipbones__ALLsup.o Vzipsystem__ALLsup.o
Vdiv_classes.mk Vzipbones_classes.mk Vzipsystem_classes.mk
Vdiv.cpp Vzipbones.cpp Vzipsystem.cpp
Vdiv.h Vzipbones.h Vzipsystem.h
Vdiv.mk Vzipbones.mk Vzipsystem.mk
Vdiv__Syms.cpp Vzipbones__Syms.cpp Vzipsystem__Syms.cpp
Vdiv__Syms.h Vzipbones__Syms.h Vzipsystem__Syms.h
Vdiv__ver.d Vzipbones__ver.d Vzipsystem__ver.d
Vdiv__verFiles.dat Vzipbones__verFiles.dat Vzipsystem__verFiles.dat

cd zipcpu/trunk/bench/asm

pi@raspberrypi2-149 ~/zipcpu/trunk/bench/asm $ make
../../sw/zasm/zasm -I../../sw/zasm/ zipdhry.S ../../sw/lib/divs.S ../../sw/lib/divu.S stack.S -o zipdhry.z
zipdhry.S:1283: ERROR: syntax error
Offending line was:	SUB	2+d�V+d�V+30+30+3,SP
Line 591 contains an undefined symbol: PC = 0x0000007d isn't ready yet
TLINE @591
TLINE OP = STO
TLINE COND = .Z
TLINE imm = gbl_ch
TLINE opb = 12
TLINE opa = 2
Line 755 contains an undefined symbol: PC = 0x000000a4 isn't ready yet
TLINE @755
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_int
TLINE opb = 12
TLINE opa = 1
Line 870 contains an undefined symbol: PC = 0x000000d6 isn't ready yet
TLINE @870
TLINE OP = STO
TLINE COND = (Always)
TLINE imm = gbl_int
TLINE opb = 12
TLINE opa = 3
Line 941 contains an undefined symbol: PC = 0x000000e0 isn't ready yet
TLINE @941
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_ptr
TLINE opb = 12
TLINE opa = 2
Line 955 contains an undefined symbol: PC = 0x000000e4 isn't ready yet
TLINE @955
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_int
TLINE opb = 12
TLINE opa = 1
Line 996 contains an undefined symbol: PC = 0x000000f5 isn't ready yet
TLINE @996
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_ch
TLINE opb = 12
TLINE opa = 4
Line 1016 contains an undefined symbol: PC = 0x000000f6 isn't ready yet
TLINE @1016
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_int
TLINE opb = 12
TLINE opa = 5
Line 1082 contains an undefined symbol: PC = 0x00000110 isn't ready yet
TLINE @1082
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_ptr
TLINE opb = 12
TLINE opa = 7
Line 1160 contains an undefined symbol: PC = 0x00000130 isn't ready yet
TLINE @1160
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_ptr
TLINE opb = 12
TLINE opa = 5
Line 1183 contains an undefined symbol: PC = 0x00000139 isn't ready yet
TLINE @1183
TLINE OP = LOD
TLINE COND = (Always)
TLINE imm = gbl_ptr
TLINE opb = 12
TLINE opa = 6
Not all symbols defined!
�../../sw/zasm/zasm -I../../sw/zasm/ testdiv.S ../../sw/lib/divs.S ../../sw/lib/divu.S stack.S -o testdiv.z
../../sw/zasm/zasm -I../../sw/zasm/ wdt.S -o wdt.z
make: *** No rule to make target 'halttest.S', needed by 'halttest.z'. Stop.

pi@raspberrypi2-149 ~/zipcpu/trunk/bench/asm $ ls
helloworld.S lodsto.S pcpc.S testdiv.S wdt.z
ivec.S Makefile poptest.s testdiv.z zipdhry.S
lfsr.S nullpc.s stack.S wdt.S zipdhry.z

cd zipcpu/trunk/bench/cpp

The Makefile requires modifications. This is based on how verilator is installed.

diff --git a/zipcpu/trunk/bench/cpp/Makefile b/zipcpu/trunk/bench/cpp/Makefile
index 8122e4f..c334478 100644
--- a/zipcpu/trunk/bench/cpp/Makefile
+++ b/zipcpu/trunk/bench/cpp/Makefile
@@ -40,9 +40,9 @@ CXX := g++
 FLAGS := -Wall -Og -g
 ZASM := ../../sw/zasm
 RTLD := ../../rtl
-INCS := -I$(RTLD)/obj_dir/ -I$(RTLD) -I/usr/share/verilator/include -I$(ZASM)
+INCS := -I$(RTLD)/obj_dir/ -I$(RTLD) -I/usr/local/share/verilator/include -I$
 SOURCES := zippy_tb.cpp memsim.cpp twoc.cpp $(ZASM)/zopcodes.cpp $(ZASM)/zparse
-VLIB := /usr/share/verilator/include/verilated.cpp
+VLIB := /usr/local/share/verilator/include/verilated.cpp
 RAWLIB := $(VLIB) $(RTLD)/obj_dir/Vzipsystem__ALL.a
 LIBS := $(RAWLIB) -lncurses
 TESTF := $(ZASM)/z.out

make
g++ -Wall -Og -g -I../../rtl/obj_dir/ -I../../rtl -I/usr/local/share/verilator/include -I../../sw/zasm zippy_tb.cpp memsim.cpp twoc.cpp ../../sw/zasm/zopcodes.cpp ../../sw/zasm/zparser.cpp /usr/local/share/verilator/include/verilated.cpp ../../rtl/obj_dir/Vzipsystem__ALL.a -lncurses -o zippy_tb

pi@raspberrypi2-149 ~/zipcpu/trunk/bench/cpp $ ls
div_tb.cpp memsim.cpp pdump.cpp testb.h twoc.h zippy_tb.cpp
Makefile memsim.h pfile.bin twoc.cpp zippy_tb

pi@raspberrypi2-149 ~/zipcpu/trunk/bench/cpp $ xsload --usb 0 --fpga ~/tmp_svn_bld_bitfiles/toplevel.bit
Success: Bitstream in /home/pi/tmp_svn_bld_bitfiles/toplevel.bit downloaded to FPGA on XuLA2-LX9!
pi@raspberrypi2-149 ~/zipcpu/trunk/bench/cpp $ ./zippy_tb -a testfile.out
No access to testfile.out, or unknown arg

cd ~/zipcpu/trunk/sw

Next 2 steps quite some time on RPi2B. Right at 4 hrs.

bash gas-script.sh

bash gcc-script.sh

pi@raspberrypi2-146 ~/zipcpu/trunk/sw $ ls install/cross-tools/bin/
zip-addr2line zip-elfedit zip-gcc-ranlib zip-ld.bfd zip-size
zip-ar zip-g++ zip-gcov zip-nm zip-strings
zip-as zip-gcc zip-gcov-tool zip-objcopy zip-strip
zip-c++ zip-gcc-5.3.0 zip-gfortran zip-objdump
zip-c++filt zip-gcc-ar zip-gprof zip-ranlib
zip-cpp zip-gcc-nm zip-ld zip-readelf

cd zipcpu/trunk/sw/zasm

make

cd xulalx25soc/trunk/sw

Modify Makefile This change is need to point to zasm, zdump, and zpp.

diff --git a/xulalx25soc/trunk/sw/Makefile b/xulalx25soc/trunk/sw/Makefile
index 4c214c9..0cdaefb 100644
--- a/xulalx25soc/trunk/sw/Makefile
+++ b/xulalx25soc/trunk/sw/Makefile
@@ -39,7 +39,7 @@ CXX := g++
 LIBUSBINC := -I/usr/include/libusb-1.0/
 LIBUSBDIR := -L/usr/lib/x86_64-linux-gnu
 OBJDIR := obj-pc
-ZIPD := /home/dan/work/rnd/zipcpu/trunk/sw/zasm
+ZIPD := /home/pi/zipcpu/trunk/sw/zasm
 BUSSRCS := ttybus.cpp llcomms.cpp regdefs.cpp usbi.cpp
 SOURCES := ziprun.cpp zipdbg.cpp dumpsdram.cpp wbregs.cpp netusb.cpp \
        flashdrvr.cpp $(BUSSRCS)

cp ~/zipcpu/trunk/sw/zasm/zopcodes. .

make
Need to add the following to the PATH on the RPi2B.
/home/pi/zipcpu/trunk/sw/install/cross-tools/bin

/home/pi/setzipcpuPath.sh
!/bin/bash
export PATH=$PATH:/home/pi/zipcpu/trunk/sw/install/cross-tools/bin:/home/pi/xulalx25soc/trunk/sw
echo $PATH
/home/pi/xulalx25soc/trunk/sw

Setting the PATH
 . ./setzipcpuPath.sh

If the toplevel.bit has been installed on XulA2-LX9

Need to modify the Makefile in ~/xulalx25soc/trunk/bench/asm
A modified version is available in ~/svn/RPi2B repository

pi@raspberrypi2-146 ~/xulalx25soc/trunk/bench/asm $ cp ~/svn/RPi2B/xulalx25soc/trunk/bench/asm/Makefile .

pi@raspberrypi2-146 ~/xulalx25soc/trunk/bench/asm $ diff -u Makefile ~/svn/xulalx25soc/trunk/bench/asm/Makefile
--- Makefile	2016-03-15 11:54:04.424471629 +0000
+++ /home/pi/svn/xulalx25soc/trunk/bench/asm/Makefile	2016-03-13 13:32:48.163373705 +0000
@@ -32,7 +32,7 @@
 ##
 ##
 all: memtest.z
-ZIPD := $(HOME)/zipcpu/trunk
+ZIPD := $(HOME)/work/rnd/zipcpu/trunk
 ZASM := $(ZIPD)/sw/zasm/zasm
 ZDUMP:= $(ZIPD)/sw/zasm/zdump

Note : Modfified the ~/xulalx25soc/trunk/bench/cpp/Makefile
pi@raspberrypi2-146 ~/xulalx25soc/trunk/bench/cpp $ diff -u ~/svn/xulalx25soc/trunk/bench/cpp/Makefile Makefile
--- /home/pi/svn/xulalx25soc/trunk/bench/cpp/Makefile	2016-03-15 20:00:20.152780348 +0000
+++ Makefile	2016-03-15 21:06:03.750107964 +0000
@@ -3,7 +3,7 @@
 OBJDIR := obj-pc
 YYMMDD := `date +%Y%m%d`
 VOBJDR := ../../rtl/obj_dir
-VROOT := /usr/share/verilator
+VROOT := /usr/local/share/verilator
 VINC := -I$(VROOT)/include -I$(VOBJDR)
 CFLAGS := -c -g -Wall -I. $(VINC)
 #
xulalx25soc/trank/bench/cpp
VROOT := /usr/share/verilator	VROOT := /usr/local/share/verilator

pi@raspberrypi2-146 ~ $ xsload --usb 0 --fpga ~/toplevel.bit
Success: Bitstream in /home/pi/toplevel.bit downloaded to FPGA on XuLA2-LX9!

 pi@raspberrypi2-146 ~ $ wbregs version
00000101 ( VERSION) : [....] 20160609

pi@raspberrypi2-146 ~ $ usbtst
Current configuration is 1
Successfully sent RESET_TO_USER_DR!
Successfully sent request for TDO bits!
Successfully read 26 bytes from port!
 0: 30 30 30 30 -- 0000
 4: 0a ff ff ff -- ....
 8: ff ff ff ff -- ....
12: ff ff ff ff -- ....
16: ff ff ff ff -- ....
20: ff ff ff ff -- ....
24: ff ff 00 00 -- ....

C Compiler for ZIPCPU RPi2B

pi@raspberrypi2-146 ~ $ cd test_zipcpu/

pi@raspberrypi2-146 ~/test_zipcpu $ . ~/setzipcpuPath.sh

pi@raspberrypi2-146 ~/test_zipcpu $ zip-gcc -nostdlib h2.c -o h2 -T xulalink.x

pi@raspberrypi2-146 ~/test_zipcpu $ zip-objdump -d h2 > dis.txt

pi@raspberrypi2-146 ~/test_zipcpu $ xsload --usb 0 --fpga ~/toplevel.bit
Success: Bitstream in /home/pi/toplevel.bit downloaded to FPGA on XuLA2-LX9!

pi@raspberrypi2-146 ~/test_zipcpu $ ziprun h2
Halting the CPU
Clearing the cache
The CPU should be fully loaded, you may now start
it. To start the CPU, type wbregs cpu 0

pi@raspberrypi2-146 ~/test_zipcpu $ wbregs cpu 0
01000000 ( ZIPCTRL)-> 00000000

pi@raspberrypi2-146 ~/test_zipcpu $ zipstate
0x00000200:

pi@raspberrypi2-146 ~/test_zipcpu $ zipdbg

Peripherals CPU State: 0x00000613 Supervisor mode
>PIC > 0x00000100< WDT : 0x00000900 WBUS: 0x00000000 PIC2: 0x00000000
 TMRA: 0x00000000 TMRB: 0x00000000 TMRC: 0x00000000 JIF : 0x00000000
 MTSK: 0x00003ffd MOST: 0x00003ffa MPST: 0x00000000 MICT: 0x00002012

Supervisor Registers
 sR0 : 0x00000100 sR1 : 0x00000900 sR2 : 0x00000000 sR3 : 0x00000000
 sR4 : 0x00000000 sR5 : 0x00000000 sR6 : 0x00000000 sR7 : 0x00000000
 sR8 : 0x00000000 sR9 : 0x00000000 sR10: 0x00000000 sR11: 0x00000000
 sR12: 0x00003ffd sSP : 0x00003ffa sCC : sPC : 0x00002012
User Registers
 uR0 : 0x00000000 uR1 : 0x00000000 uR2 : 0x00000000 uR3 : 0x00000000
 uR4 : 0x00000000 uR5 : 0x00000000 uR6 : 0x00000000 uR7 : 0x00000000
 uR8 : 0x00000000 uR9 : 0x00000000 uR10: 0x00000000 uR11: 0x00000000
 uR12: 0x00000000 uSP : 0x00000000 uCC : uPC : 0x00000000

 0x00002015 0x0c873ffe LOD $-2(R12),R1 >00003ffa 0x00000000
 0x00002014 0x789bfffd BNZ $-3 00003ffb 0x00002029
 0x00002013 0x0c000000 CMP $0,R1 00003ffc 0x00000000
>0x00002012 0x0c84000b LOD $11(R0),R1 00003ffd 0x00000000
 0x00002011 0x7e000000 NOOP 00003ffe 0x00000000

Appendix F. The zip-objdump -d h2

h2: file format elf32-zip

Disassembly of section .rocode:

00002000 <_start>:
    2000:	6b 00 00 00	LDI 0x00003fff,SP	// 3fff <_top_of_stack>
    2001:	6a 40 3f ff
    2002:	7c 87 c0 00	LJMP @0x00002004	// 2004 <entry>
    2003:	00 00 20 04

00002004 <entry>:
    2004:	68 00 00 02	SUB $2,SP
    2005:	04 c7 40 00	STO R0,(SP)
    2006:	2c c7 40 01	STO R5,$1(SP)
    2007:	0b 00 01 00	BREV $256,R1
    2008:	03 c3 c0 02	MOV $2+PC,R0
    2009:	7c 87 c0 00	LJMP @0x00002065	// 2065 <zip_clear_sdram>
    200a:	00 00 20 65
    200b:	0d 80 00 4f	LDI $79,R1
    200c:	0c c0 01 07	STO R1,($263)
    200d:	13 00 00 00	LDI 0x00002097,R2	// 2097 <msg>
    200e:	12 40 20 97
    200f:	1c 84 80 00	LOD (R2),R3
    2010:	1c 00 00 00	CMP $0,R3
    2011:	78 98 00 12	BNZ @0x00002024	// 2024 <entry+0x20>
    2012:	2b 00 40 02	LDI 0x40024002,R5	// 40024002 <_top_of_heap+0x3f124002>
    2013:	2a 40 40 02
    2014:	2c c0 01 06	STO R5,($262)
    2015:	0b 00 01 00	BREV $256,R1
    2016:	03 c3 c0 02	MOV $2+PC,R0
    2017:	7c 87 c0 00	LJMP @0x00002034	// 2034 <zip_read_image>
    2018:	00 00 20 34
    2019:	28 83 bf fe	ADD $-16386,R5
    201a:	2c c0 01 06	STO R5,($262)
    201b:	0b 00 01 00	BREV $256,R1
    201c:	03 c3 c0 02	MOV $2+PC,R0
    201d:	7c 87 c0 00	LJMP @0x00002071	// 2071 <dwt_process>
    201e:	00 00 20 71
    201f:	03 c3 c0 02	MOV $2+PC,R0
    2020:	7c 87 c0 00	LJMP @0x0000206e	// 206e <dwt_steps>
    2021:	00 00 20 6e
    2022:	14 80 01 10	LOD ($272),R2
    2023:	78 80 00 09	BRA @0x0000202d	// 202d <entry+0x29>
    2024:	0c 80 01 0b	LOD ($267),R1
    2025:	0c 00 00 00	CMP $0,R1
    2026:	78 9b ff fd	BNZ @0x00002024	// 2024 <entry+0x20>
    2027:	10 80 00 01	ADD $1,R2
    2028:	1c c0 01 0b	STO R3,($267)
    2029:	1c 84 80 00	LOD (R2),R3
    202a:	1c 00 00 00	CMP $0,R3
    202b:	78 9b ff f8	BNZ @0x00002024	// 2024 <entry+0x20>
    202c:	78 83 ff e5	BRA @0x00002012	// 2012 <entry+0xe>
    202d:	0c 80 01 10	LOD ($272),R1
    202e:	14 04 40 00	CMP R1,R2
    202f:	78 93 ff fd	BZ @0x0000202d	// 202d <entry+0x29>
    2030:	04 87 40 00	LOD (SP),R0
    2031:	2c 87 40 01	LOD 1(SP),R5
    2032:	68 80 00 02	ADD $2,SP
    2033:	7b c0 00 00	JMP R0

00002034 <zip_read_image>:
    2034:	68 00 00 05	SUB $5,SP
    2035:	2c c7 40 00	STO R5,(SP)
    2036:	34 c7 40 01	STO R6,$1(SP)
    2037:	3c c7 40 02	STO R7,$2(SP)
    2038:	44 c7 40 03	STO R8,$3(SP)
    2039:	4c c7 40 04	STO R9,$4(SP)
    203a:	25 80 00 00	CLR R4
    203b:	24 c0 01 04	STO R4,($260)
    203c:	15 81 00 01	LDI $65537,R2
    203d:	14 c0 01 06	STO R2,($262)
    203e:	2b c0 40 00	MOV R1,R5
    203f:	45 ff ff ff	LDI $-1,R8
    2040:	3b 00 c1 00	BREV $49408,R7
    2041:	35 81 00 00	LDI $65536,R6
    2042:	44 c4 40 00	STO R8,(R1)
    2043:	14 80 01 0a	LOD ($266),R2
    2044:	1b c0 80 00	MOV R2,R3
    2045:	18 40 01 00	AND $256,R3
    2046:	78 9b ff fc	BNZ @0x00002043	// 2043 <zip_read_image+0xf>
    2047:	11 80 00 14	LSL $20,R2
    2048:	1c 80 01 0a	LOD ($266),R3
    2049:	4b c0 c0 00	MOV R3,R9
    204a:	48 40 01 00	AND $256,R9
    204b:	78 9b ff fc	BNZ @0x00002048	// 2048 <zip_read_image+0x14>
    204c:	19 80 00 0a	LSL $10,R3
    204d:	10 c4 c0 00	OR R3,R2
    204e:	1c 80 01 0a	LOD ($266),R3
    204f:	4b c0 c0 00	MOV R3,R9
    2050:	48 40 01 00	AND $256,R9
    2051:	78 9b ff fc	BNZ @0x0000204e	// 204e <zip_read_image+0x1a>
    2052:	10 c4 c0 00	OR R3,R2
    2053:	14 c5 40 00	STO R2,(R5)
    2054:	24 c5 c0 00	STO R4,(R7)
    2055:	34 c0 01 06	STO R6,($262)
    2056:	14 80 01 02	LOD ($258),R2
    2057:	10 40 01 00	AND $256,R2
    2058:	78 98 00 05	BNZ @0x0000205e	// 205e <zip_read_image+0x2a>
    2059:	20 80 00 01	ADD $1,R4
    205a:	28 80 00 01	ADD $1,R5
    205b:	08 80 00 02	ADD $2,R1
    205c:	24 01 00 00	CMP $65536,R4
    205d:	78 9b ff e4	BNZ @0x00002042	// 2042 <zip_read_image+0xe>
    205e:	2c 87 40 00	LOD (SP),R5
    205f:	34 87 40 01	LOD 1(SP),R6
    2060:	3c 87 40 02	LOD 2(SP),R7
    2061:	44 87 40 03	LOD 3(SP),R8
    2062:	4c 87 40 04	LOD 4(SP),R9
    2063:	68 80 00 05	ADD $5,SP
    2064:	7b c0 00 00	JMP R0

00002065 <zip_clear_sdram>:
    2065:	15 83 00 00	LDI $196608,R2
    2066:	1b c0 40 00	MOV R1,R3
    2067:	18 84 80 00	ADD R2,R3
    2068:	15 80 00 00	CLR R2
    2069:	08 80 00 01	ADD $1,R1
    206a:	14 c4 7f ff	STO R2,$-1(R1)
    206b:	0c 04 c0 00	CMP R3,R1
    206c:	78 9b ff fc	BNZ @0x00002069	// 2069 <zip_clear_sdram+0x4>
    206d:	7b c0 00 00	JMP R0

0000206e <dwt_steps>:
    206e:	0d 81 00 01	LDI $65537,R1
    206f:	0c c0 01 06	STO R1,($262)
    2070:	7b c0 00 00	JMP R0

00002071 <dwt_process>:
    2071:	68 00 00 02	SUB $2,SP
    2072:	2c c7 40 00	STO R5,(SP)
    2073:	34 c7 40 01	STO R6,$1(SP)
    2074:	1c 84 80 07	LOD 7(R2),R3
    2075:	19 c0 00 14	ASR $20,R3
    2076:	24 84 80 08	LOD 8(R2),R4
    2077:	21 c0 00 14	ASR $20,R4
    2078:	14 84 80 09	LOD 9(R2),R2
    2079:	11 c0 00 14	ASR $20,R2
    207a:	35 81 00 00	LDI $65536,R6
    207b:	34 c0 01 06	STO R6,($262)
    207c:	1c c4 40 06	STO R3,$6(R1)
    207d:	24 c4 40 07	STO R4,$7(R1)
    207e:	14 c4 40 08	STO R2,$8(R1)
    207f:	18 84 80 00	ADD R2,R3
    2080:	19 c0 00 01	ASR $1,R3
    2081:	20 04 c0 00	SUB R3,R4
    2082:	24 c4 40 09	STO R4,$9(R1)
    2083:	2c 87 40 00	LOD (SP),R5
    2084:	34 87 40 01	LOD 1(SP),R6
    2085:	68 80 00 02	ADD $2,SP
    2086:	7b c0 00 00	JMP R0

00002087 <msg1>:
    2087:	00 00 00 44 00 00 00 61 00 00 00 74 00 00 00 61 ...D...a...t...a
    208b:	00 00 00 20 00 00 00 72 00 00 00 64 00 00 00 79 ... ...r...d...y
    208f:	00 00 00 20 00 00 00 20 00 00 00 20 00 00 00 20 ... ... ... ...
    2093:	00 00 00 20 00 00 00 0d 00 00 00 0a 00 00 00 00 ... ............

00002097 <msg>:
    2097:	00 00 00 48 00 00 00 65 00 00 00 6c 00 00 00 6c ...H...e...l...l
    209b:	00 00 00 6f 00 00 00 2c 00 00 00 20 00 00 00 77 ...o...,... ...w
    209f:	00 00 00 6f 00 00 00 72 00 00 00 6c 00 00 00 64 ...o...r...l...d
    20a3:	00 00 00 21 00 00 00 0d 00 00 00 0a 00 00 00 00 ...!............

000020a7 <XULA_BUSY>:
    20a7:	40 00 00 00 @...

000020a8 <READY_FOR_XMIT>:
    20a8:	40 00 40 00 @.@.

000020a9 <LED_OFF>:
    20a9:	00 02 00 00 ....

000020aa <LED_ON>:
    20aa:	00 02 00 02 ....

Appendix G Ubuntu zipcu & xulalx25soc software build.

vidal@ws009:~/wkg$ cp -R svn/xulalx25soc .

vidal@ws009:~/wkg$ cp -R svn/zipcpu/ .

vidal@ws009:~/wkg$ cd zipcpu/trunk/

vidal@ws009:~/wkg/zipcpu/trunk$ ls rtl/obj_dir/
Vdiv__ALL.a Vzipbones__ALL.a Vzipsystem__ALL.a
Vdiv__ALLcls.cpp Vzipbones__ALLcls.cpp Vzipsystem__ALLcls.cpp
Vdiv__ALLcls.d Vzipbones__ALLcls.d Vzipsystem__ALLcls.d
Vdiv__ALLcls.o Vzipbones__ALLcls.o Vzipsystem__ALLcls.o
Vdiv__ALLsup.cpp Vzipbones__ALLsup.cpp Vzipsystem__ALLsup.cpp
Vdiv__ALLsup.d Vzipbones__ALLsup.d Vzipsystem__ALLsup.d
Vdiv__ALLsup.o Vzipbones__ALLsup.o Vzipsystem__ALLsup.o
Vdiv_classes.mk Vzipbones_classes.mk Vzipsystem_classes.mk
Vdiv.cpp Vzipbones.cpp Vzipsystem.cpp
Vdiv.h Vzipbones.h Vzipsystem.h
Vdiv.mk Vzipbones.mk Vzipsystem.mk
Vdiv__Syms.cpp Vzipbones__Syms.cpp Vzipsystem__Syms.cpp
Vdiv__Syms.h Vzipbones__Syms.h Vzipsystem__Syms.h
Vdiv__ver.d Vzipbones__ver.d Vzipsystem__ver.d
Vdiv__verFiles.dat Vzipbones__verFiles.dat Vzipsystem__verFiles.dat

vidal@ws009:~/wkg/zipcpu/trunk$ cd sw/

vidal@ws009:~/wkg/zipcpu/trunk/sw$ bash gas-script.sh

vidal@ws009:~/wkg/zipcpu/trunk/sw$ bash gcc-script.sh

vidal@ws009:~/wkg/zipcpu/trunk/sw$ cd ~/wkg/xulalx25soc/trunk/bench/cpp/

vidal@ws009:~/wkg/xulalx25soc/trunk$ make
bash -c 'if [ ! -e `date +%Y%m%d`-build.v ]; then perl xilinx/mkdatev.pl > `date +%Y%m%d`-build.v; rm -f rtl/builddate.v; fi'
bash -c 'if [ ! -e rtl/builddate.v ]; then cd rtl; ln -fs ../`date +%Y%m%d`-build.v builddate.v; fi'
cd rtl ; make --no-print-directory
verilator -cc -y cpu busmaster.v
cd ./obj_dir; make -f Vbusmaster.mk
/usr/bin/perl /usr/local/share/verilator/bin/verilator_includer -DVL_INCLUDE_OPT=include Vbusmaster.cpp > Vbusmaster__ALLcls.cpp
g++ -I. -MMD -I/usr/local/share/verilator/include -I/usr/local/share/verilator/include/vltstd -DVL_PRINTF=printf -DVM_TRACE=0 -DVM_COVERAGE=0 -Wno-char-subscripts -Wno-parentheses-equality -Wno-sign-compare -Wno-uninitialized -Wno-unused-but-set-variable -Wno-unused-parameter -Wno-unused-variable -c -o Vbusmaster__ALLcls.o Vbusmaster__ALLcls.cpp
/usr/bin/perl /usr/local/share/verilator/bin/verilator_includer -DVL_INCLUDE_OPT=include Vbusmaster__Syms.cpp > Vbusmaster__ALLsup.cpp
g++ -I. -MMD -I/usr/local/share/verilator/include -I/usr/local/share/verilator/include/vltstd -DVL_PRINTF=printf -DVM_TRACE=0 -DVM_COVERAGE=0 -Wno-char-subscripts -Wno-parentheses-equality -Wno-sign-compare -Wno-uninitialized -Wno-unused-but-set-variable -Wno-unused-parameter -Wno-unused-variable -c -o Vbusmaster__ALLsup.o Vbusmaster__ALLsup.cpp
      Archiving Vbusmaster__ALL.a ...
ar r Vbusmaster__ALL.a Vbusmaster__ALLcls.o Vbusmaster__ALLsup.o
ar: creating Vbusmaster__ALL.a
ranlib Vbusmaster__ALL.a
cd xilinx ; make --no-print-directory xula.bit
Makefile:105: warning: overriding commands for target `obj-xilinx/xula.ncd'
Makefile:101: warning: ignoring old commands for target `obj-xilinx/xula.ncd'
make[1]: *** No rule to make target `obj-xilinx/xula_map.ncd', needed by `obj-xilinx/xula.ncd'. Stop.
make: *** [bit] Error 2

Note : Modfified the ~/wkg/xulalx25soc/trunk/bench/cpp/Makefile
vidal@ws009:~/wkg/xulalx25soc/trunk/bench/cpp$ diff -u ~/wkg/svn/xulalx25soc/trunk/bench/cpp/Makefile Makefile
--- /home/vidal/wkg/svn/xulalx25soc/trunk/bench/cpp/Makefile	2016-03-15 13:54:20.832344980 -0600
+++ Makefile	2016-03-15 15:19:40.656287586 -0600
@@ -3,7 +3,7 @@
 OBJDIR := obj-pc
 YYMMDD := `date +%Y%m%d`
 VOBJDR := ../../rtl/obj_dir
-VROOT := /usr/share/verilator
+VROOT := /usr/local/share/verilator
 VINC := -I$(VROOT)/include -I$(VOBJDR)
 CFLAGS := -c -g -Wall -I. $(VINC)
 #

VROOT := /usr/share/verilator	VROOT := /usr/local/share/verilator

vidal@ws009:~/wkg/xulalx25soc/trunk$ cd bench/cpp/
vidal@ws009:~/wkg/xulalx25soc/trunk/bench/cpp$ make
g++ -c -g -Wall -I. -I/usr/local/share/verilator/include -I../../rtl/obj_dir busmaster_tb.cpp -o obj-pc/busmaster_tb.o
In file included from busmaster_tb.cpp:28:0:
pipecmdr.h: In instantiation of ‘void PIPECMDR<VA>::tick() [with VA = Vbusmasterr]’:
busmaster_tb.cpp:78:13: required from here
pipecmdr.h:179:57: warning: comparison between signed and unsigned integer expressions [-Wsign-compare]
    if ((TESTB<VA>::m_core->o_tx_data == '\n')||(m_txpos >= sizeof(m_txbuf))) {
        ^
g++ -c -g -Wall -I. -I/usr/local/share/verilator/include -I../../rtl/obj_dir sdramsim.cpp -o obj-pc/sdramsim.o
g++ -c -g -Wall -I. -I/usr/local/share/verilator/include -I../../rtl/obj_dir qspiflashsim.cpp -o obj-pc/qspiflashsim.o
g++ -c -g -Wall -I. -I/usr/local/share/verilator/include -I../../rtl/obj_dir /usr/local/share/verilator/include/verilated.cpp -o obj-pc/verilated.o
g++ -g -o busmaster_tb obj-pc/busmaster_tb.o obj-pc/sdramsim.o obj-pc/qspiflashsim.o obj-pc/verilated.o ../../rtl/obj_dir/Vbusmaster__ALL.a
tar --transform s,^,`date +%Y%m%d`-bench-cpp/, -chjf `date +%Y%m%d`-bench-cpp.tjz Makefile *.cpp *.h

vidal@ws009:~/wkg/xulalx25soc/trunk/bench/cpp$ cd ../../sw/

vidal@ws009:~/wkg/xulalx25soc/trunk/sw$ cp ../../../zipcpu/trunk/sw/zasm/zparser.h .

vidal@ws009:~/wkg/xulalx25soc/trunk/sw$ cp ../../../zipcpu/trunk/sw/zasm/zopcodes.h .

Note : Modfified the ~/wkg/xulalx25soc/trunk/sw/Makefile
vidal@ws009:~/wkg/xulalx25soc/trunk/sw$ diff -u ~/wkg/svn/xulalx25soc/trunk/sw/Makefile Makefile
--- /home/vidal/wkg/svn/xulalx25soc/trunk/sw/Makefile	2016-03-15 13:54:26.280344919 -0600
+++ Makefile	2016-03-15 16:01:25.320259508 -0600
@@ -39,7 +39,7 @@
 LIBUSBINC := -I/usr/include/libusb-1.0/
 LIBUSBDIR := -L/usr/lib/x86_64-linux-gnu
 OBJDIR := obj-pc
-ZIPD := /home/dan/work/rnd/zipcpu/trunk/sw/zasm
+ZIPD := /home/vidal/wkg/zipcpu/trunk/sw/zasm
 BUSSRCS := ttybus.cpp llcomms.cpp regdefs.cpp usbi.cpp
 SOURCES := ziprun.cpp zipdbg.cpp dumpsdram.cpp wbregs.cpp netusb.cpp	\
 flashdrvr.cpp $(BUSSRCS)

make

 vidal@ws009:~/wkg/xulalx25soc/trunk/sw$ ls
cfgscope flashdrvr.h ramscope.cpp usbi.h ziprun
cfgscope.cpp llcomms.cpp regdefs.cpp usbtst ziprun.cpp
cpuscope.cpp llcomms.h regdefs.h usbtst.cpp zipstate
devbus.h Makefile ttybus.cpp wbregs zipstate.cpp
dumpflash netusb ttybus.h wbregs.cpp zopcodes.h
dumpflash.cpp netusb.cpp twoc.cpp wbsettime zparser.h
dumpsdram obj-pc twoc.h wbsettime.cpp
dumpsdram.cpp port.h txtest.cpp zipdbg
flashdrvr.cpp ramscope usbi.cpp zipdbg.cpp

Appendix H Ubuntu test

vidal@ws009:~$ . setzipcpuPath.sh
PATH,/home/vidal/bin:/usr/lib/lightdm/lightdm:/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin:/usr/games:/home/vidal/wkg/zipcpu/trunk/sw/install/cross-tools/bin:/home/vidal/wkg/xulalx25soc/trunk/sw

vidal@ws009:~$ which wbregs
/home/vidal/wkg/xulalx25soc/trunk/sw/wbregs

vidal@ws009:~$ which zip-gcc
/home/vidal/wkg/zipcpu/trunk/sw/install/cross-tools/bin/zip-gcc

vidal@ws009:~$ xsload --usb 0 --fpga ~/wkg/svn/test_xula2soc/toplevel.bit
Success: Bitstream in /home/vidal/wkg/svn/test_xula2soc/toplevel.bit downloaded to FPGA on XuLA2-LX9!

vidal@ws009:~$ cd ~/wkg/test_zipcpu/

vidal@ws009:~/wkg/test_zipcpu$ zip-gcc -nostdlib h2.c -o h2 -T xulalink.x

vidal@ws009:~/wkg/test_zipcpu$ zip-objdump -d h2 > dis.txt

vidal@ws009:~/wkg/test_zipcpu$ zip-objdump -d h2 > dis.txt

h2: file format elf32-zip

Disassembly of section .rocode:

00002000 <_start>:
    2000:	6a 00 00 00	LDIHI $0,SP
    2001:	6a 40 3f ff	LDILO $16383,SP
    2002:	7c 87 c0 00	LJMP
    2003:	00 00 20 04

00002004 <entry>:
    2004:	68 00 00 04	SUB $4,SP
    2005:	04 c7 40 02	STO R0,$2(SP)
    2006:	64 c7 40 03	STO R12,$3(SP)
    2007:	63 c3 40 02	MOV $2+SP,R12
    2008:	05 80 01 00	LDI $256,R0
    2009:	0d 80 20 8d	LDI $8333,R1
    200a:	0c c4 00 06	STO R1,$6(R0)
    200b:	0a 00 00 00	LDIHI $0,R1
    200c:	0a 40 20 24	LDILO $8228,R1
    200d:	0c c7 3f ff	STO R1,$-1(R12)
    200e:	78 80 00 09	BRA @0x00002018
    200f:	7e 00 00 00	NOOP
    2010:	0c 84 00 0a	LOD $10(R0),R1
    2011:	0c 00 00 00	CMP $0,R1
    2012:	78 9b ff fd	BNZ @0x00002010
    2013:	0c 87 3f ff	LOD $-1(R12),R1
    2014:	13 c0 40 01	MOV $1+R1,R2
    2015:	14 c7 3f ff	STO R2,$-1(R12)
    2016:	0c 84 40 00	LOD (R1),R1
    2017:	0c c4 00 0a	STO R1,$10(R0)
    2018:	0c 87 3f ff	LOD $-1(R12),R1
    2019:	0c 84 40 00	LOD (R1),R1
    201a:	0c 00 00 00	CMP $0,R1
    201b:	78 9b ff f3	BNZ @0x0000200f
    201c:	0c 84 00 0f	LOD $15(R0),R1
    201d:	0c c7 3f fe	STO R1,$-2(R12)
    201e:	7e 00 00 00	NOOP
    201f:	14 84 00 0f	LOD $15(R0),R2
    2020:	0c 87 3f fe	LOD $-2(R12),R1
    2021:	14 04 40 00	CMP R1,R2
    2022:	78 93 ff fc	BRZ @0x0000201f
    2023:	78 83 ff e7	BRA @0x0000200b

00002024 <msg>:
    2024:	00 00 00 48 00 00 00 65 00 00 00 6c 00 00 00 6c ...H...e...l...l
    2028:	00 00 00 6f 00 00 00 2c 00 00 00 20 00 00 00 77 ...o...,... ...w
    202c:	00 00 00 6f 00 00 00 72 00 00 00 6c 00 00 00 64 ...o...r...l...d
    2030:	00 00 00 21 00 00 00 0a 00 00 00 00 ...!........

vidal@ws009:~/wkg/test_zipcpu$ ziprun h2
Halting the CPU
Clearing the cache
The CPU should be fully loaded, you may now start
it. To start the CPU, type wbregs cpu 0

vidal@ws009:~/wkg/test_zipcpu$ wbregs cpu 0
01000000 ( ZIPCTRL)-> 00000000

Appendix I. SDRAM test

pi@raspberrypi2-149 ~/xulalx25soc/trunk/sw $ . ~/setzipcpuPath.sh
PATH,/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin:/usr/local/games:/usr/games:/home/pi/zipcpu/trunk/sw/install/cross-tools/bin:/home/pi/xulalx25soc/trunk/sw

pi@raspberrypi2-149 ~ $ xsload --usb 0 --fpga tmp_svn_bld_bitfiles/toplevel.bit Success: Bitstream in tmp_svn_bld_bitfiles/toplevel.bit downloaded to FPGA on XuLA2-LX9!

pi@raspberrypi2-149 ~ $ od -x jpeg-2000-test/pc_fast_blinker_jpeg/input_examples/data_to_fpga.bin
0000000 913a a448 913a 9c38 713a a438 913a 9c38
0000020 713a 9c38 713a 9c38 713a 9c38 713a 9c38
0000040 713a 9c38 713a a448 913a a448 913a a448
0000060 913a 9c48 713a a448 913a a438 913a a458
0000100 913a ac48 b13a ac58 b13a a458 913a a448
0000120 913a 9438 513a 8428 103a 7cf8 f039 5cd8
0000140 7039 54a8 5039 54a8 5039 5cb8 7039 5ca8
0000160 7039 64b8 9039 5ca8 7039 5cb8 7039 64b8
0000200 9039 64b8 9039 64c8 9039 64c8 9039 64c8
0000220 9039 6cc8 b039 64b8 9039 64c8 9039 5cc8
0000240 7039 64c8 9039 64b8 9039 64c8 9039 64c8
0000260 9039 64c8 9039 5cc8 7039 6cc8 b039 6cd8
0000300 b039 6cd8 b039 6cc8 b039 74c8 d039 6cd8
0000320 b039 6cd8 b039 6cd8 b039 64c8 9039 64d8
0000340 9039 6cd8 b039 6cd8 b039 64c8 9039 64c8
0000360 9039 5cc8 7039 6cc8 b039 64c8 9039 64b8
0000400 9039 5cc8 7039 64c8 9039 6cc8 b039 64c8
0000420 9039 64d8 9039 64d8 9039 64c8 9039 54b8
0000440 5039 54b8 5039 5498 5039 4ca8 3039 5498
0000460 5039 54a8 5039 54a8 5039 5ca8 7039 5ca8
0000500 7039 4ca8 3039 4c98 3039 5498 5039 4c98
0000520 3039 4c88 3039 4498 1039 3c88 f038 3478
0000540 d038 3478 d038 3478 d038 3488 d038 3468
0000560 d038 2c68 b038 2c58 b038 3468 d038 3458
0000600 d038 3458 d038 4468 1039 7cc8 f139 8c08
0000620 313a 8c18 313a 7c08 f139 6408 9039 3488
0000640 d038 2448 9038 2438 9038 2448 9038 2448
0000660 9038 1c48 7038 2438 9038 1c38 7038 2438
0000700 9038 2c48 b038 2458 9038 2458 9038 1c48
0000720 7038 2c48 b038 2c68 b038 5c88 7039 54a8
0000740 5039 4488 1039 2c68 b038 3458 d038 3468
0000760 d038 3468 d038 3468

pi@raspberrypi2-149 ~ $ dumpsdram jpeg-2000-test/pc_fast_blinker_jpeg/input_examples/data_to_fpga.bin rd_data_dumpsdram
ARG[0] = jpeg-2000-test/pc_fast_blinker_jpeg/input_examples/data_to_fpga.bin
ARG[1] = rd_data_dumpsdram
SUCCESS::fully wrote full file to memory (pos = 0080007e)
nr = 127, pos = 0080007f (00800000 / 01000000)
Only read 126 words from our input file
Successfully read&copied 007f ( 127) words from memory

pi@raspberrypi2-149 ~ $ od -x rd_data_dumpsdram
0000000 913a a448 913a 9c38 713a a438 913a 9c38
0000020 713a 9c38 713a 9c38 713a 9c38 713a 9c38
0000040 713a 9c38 713a a448 913a a448 913a a448
0000060 913a 9c48 713a a448 913a a438 913a a458
0000100 913a ac48 b13a ac58 b13a a458 913a a448
0000120 913a 9438 513a 8428 103a 7cf8 f039 5cd8
0000140 7039 54a8 5039 54a8 5039 5cb8 7039 5ca8
0000160 7039 64b8 9039 5ca8 7039 5cb8 7039 64b8
0000200 9039 64b8 9039 64c8 9039 64c8 9039 64c8
0000220 9039 6cc8 b039 64b8 9039 64c8 9039 5cc8
0000240 7039 64c8 9039 64b8 9039 64c8 9039 64c8
0000260 9039 64c8 9039 5cc8 7039 6cc8 b039 6cd8
0000300 b039 6cd8 b039 6cc8 b039 74c8 d039 6cd8
0000320 b039 6cd8 b039 6cd8 b039 64c8 9039 64d8
0000340 9039 6cd8 b039 6cd8 b039 64c8 9039 64c8
0000360 9039 5cc8 7039 6cc8 b039 64c8 9039 64b8
0000400 9039 5cc8 7039 64c8 9039 6cc8 b039 64c8
0000420 9039 64d8 9039 64d8 9039 64c8 9039 54b8
0000440 5039 54b8 5039 5498 5039 4ca8 3039 5498
0000460 5039 54a8 5039 54a8 5039 5ca8 7039 5ca8
0000500 7039 4ca8 3039 4c98 3039 5498 5039 4c98
0000520 3039 4c88 3039 4498 1039 3c88 f038 3478
0000540 d038 3478 d038 3478 d038 3488 d038 3468
0000560 d038 2c68 b038 2c58 b038 3468 d038 3458
0000600 d038 3458 d038 4468 1039 7cc8 f139 8c08
0000620 313a 8c18 313a 7c08 f139 6408 9039 3488
0000640 d038 2448 9038 2438 9038 2448 9038 2448
0000660 9038 1c48 7038 2438 9038 1c38 7038 2438
0000700 9038 2c48 b038 2458 9038 2458 9038 1c48
0000720 7038 2c48 b038 2c68 b038 5c88 7039 54a8
0000740 5039 4488 1039 2c68 b038 3458 d038 3468
0000760 d038 3468 d038 3468 1250 6355

Appendix I Notes on Update to zipcpu rev114.
Do I need new files zasm.tab.c & zasm.tab.h for Ubuntu build?

See below.

Revison 114

 make clean

make binutils

make binutils-install

No compiler

 bash gcc-script.sh

vidal@ws009:~/wkg/zipcpu/trunk/sw$ ls -la install/cross-tools/bin/

-rwxr-xr-x 1 vidal vidal 3519292 Mar 28 09:34 zip-addr2line
-rwxr-xr-x 2 vidal vidal 3698382 Mar 28 09:34 zip-ar
-rwxr-xr-x 2 vidal vidal 4863691 Mar 28 09:34 zip-as
-rwxr-xr-x 2 vidal vidal 2950108 Mar 28 09:58 zip-c++
-rwxr-xr-x 1 vidal vidal 3482006 Mar 28 09:34 zip-c++filt
-rwxr-xr-x 1 vidal vidal 2952942 Mar 28 09:58 zip-cpp
-rwxr-xr-x 1 vidal vidal 105405 Mar 28 09:34 zip-elfedit
-rwxr-xr-x 2 vidal vidal 2950108 Mar 28 09:58 zip-g++
-rwxr-xr-x 2 vidal vidal 2941530 Mar 28 09:58 zip-gcc
-rwxr-xr-x 2 vidal vidal 2941530 Mar 28 09:58 zip-gcc-5.3.0
-rwxr-xr-x 1 vidal vidal 146879 Mar 28 09:58 zip-gcc-ar
-rwxr-xr-x 1 vidal vidal 146839 Mar 28 09:58 zip-gcc-nm
-rwxr-xr-x 1 vidal vidal 146851 Mar 28 09:58 zip-gcc-ranlib
-rwxr-xr-x 1 vidal vidal 1950006 Mar 28 09:58 zip-gcov
-rwxr-xr-x 1 vidal vidal 1822554 Mar 28 09:58 zip-gcov-tool
-rwxr-xr-x 1 vidal vidal 2951263 Mar 28 09:58 zip-gfortran
-rwxr-xr-x 1 vidal vidal 4081537 Mar 28 09:34 zip-gprof
-rwxr-xr-x 4 vidal vidal 4761493 Mar 28 09:34 zip-ld
-rwxr-xr-x 4 vidal vidal 4761493 Mar 28 09:34 zip-ld.bfd
-rwxr-xr-x 2 vidal vidal 3565291 Mar 28 09:34 zip-nm
-rwxr-xr-x 2 vidal vidal 4413605 Mar 28 09:34 zip-objcopy
-rwxr-xr-x 2 vidal vidal 5055608 Mar 28 09:34 zip-objdump
-rwxr-xr-x 2 vidal vidal 3698373 Mar 28 09:34 zip-ranlib
-rwxr-xr-x 1 vidal vidal 1354642 Mar 28 09:34 zip-readelf
-rwxr-xr-x 1 vidal vidal 3514972 Mar 28 09:34 zip-size
-rwxr-xr-x 1 vidal vidal 3513435 Mar 28 09:34 zip-strings
-rwxr-xr-x 2 vidal vidal 4413660 Mar 28 09:34 zip-strip

vidal@ws009:~/wkg/zipcpu/trunk/sw$ cp ~/Downloads/opencores_dan/zasm.tab.h zasm/obj-pc/
vidal@ws009:~/wkg/zipcpu/trunk/sw$ cp ~/Downloads/opencores_dan/zasm.tab.c zasm/obj-pc/
vidal@ws009:~/wkg/zipcpu/trunk/sw$ cd zasm/

Building dependency file(s)
optest.cpp:46:2: error: #error "This file is now obsolete. The opcodes no longer match the CPU ISET."
 #error "This file is now obsolete. The opcodes no longer match the CPU ISET."
  ^
flex -o obj-pc/zasm.lex.cpp zasm.l
g++ -c -I. -Iobj-pc/ -g -O0 obj-pc/zasm.lex.cpp -o obj-pc/zasm.lex.o
g++ -c -I. -Iobj-pc/ -g -O0 obj-pc/zasm.tab.c -o obj-pc/zasm.tab.o
g++ -c -I. -g -O0 asmdata.cpp -o obj-pc/asmdata.o
g++ -o zasm -g -O0 obj-pc/zparser.o obj-pc/zopcodes.o obj-pc/twoc.o obj-pc/zasm.lex.o obj-pc/zasm.tab.o obj-pc/asmdata.o
g++ -c -g -O0 zdump.cpp -o obj-pc/zdump.o
g++ -g -O0 obj-pc/zdump.o obj-pc/zopcodes.o obj-pc/twoc.o -o zdump
flex -o obj-pc/zpp.cpp zpp.l
g++ -c -g -O0 obj-pc/zpp.cpp -o obj-pc/zpp.o
g++ -o zpp -g -O0 obj-pc/zpp.o