Developing the C Software to be used in the ZIPCPU
04/13/16

With the following command create a file to be sent to xulalx25soc or simulator.
The command reads the file lena_256.png

Using 2 dim array array does not work in the zipcpu.

img[row][col] = img[row][col] - ( (img[row-1][col] + img[row+1][col]) >> 1);
or
*(buf_ptr+col+row*256) = *(buf_ptr+col+row*256) - ((*(buf_ptr+col+(row-1)*256) + *(buf_ptr+col+(row+1)*256)) >> 1);

Even with a 1 dim array problems on the RPi2B were observed.

dum1 = *(buf_ptr+col+row*256);
dum2 = *(buf_ptr+col+(row-1)*256);
dum3 = *(buf_ptr+col+(row+1)*256);
dum4 = ((dum2 + dum3) >> 1);
dum5 = *(buf_ptr+col+row*256);
dum6 = dum5 – dum4;
The storing of the value is still causing a segmentation fault.
 *(buf_ptr+col+row*256) = dum6;

pi@mysshserver ~/jpeg-2000-test/zipcpu $ zip-gcc -fno-builtin -nostdlib -O3 dwt_steps.c -o dwt_steps -T xulalink.x
dwt_steps.c: In function 'entry':
dwt_steps.c:108:1: internal compiler error: Segmentation fault
 }
 ^
0x552807 crash_signal
../../gcc-5.3.0-zip/gcc/toplev.c:383
Please submit a full bug report,
with preprocessed source if appropriate.
Please include the complete backtrace with any bug report.
See <http://gcc.gnu.org/bugs.html> for instructions.

Another file was creaated dwt_write.c
dum7 = buf_ptr;
dwt_write(dum7,col,row,dum6);

Which writes the values back in the image.

void dwt_write(int *a, int c, int r, int v) {
int *b;
b = a;
*(a+c+r*256) = v;

}

python rd_wr_image.py used to create the file
img_to_fpga.bin
and writes the pixels as 32 bit values to be used
by zipcpu.
vidal@ws009:~/wkg/jpeg-2000-test/zipcpu$ python rd_wr_image.py

vidal@ws009:~/wkg/jpeg-2000-test/zipcpu$ od -x img_to_fpga.bin

0000000 009c 0000 009c 0000 00a4 0000 00a4 0000
0000020 00a4 0000 00a4 0000 009c 0000 00a4 0000
0000040 009c 0000 00a4 0000 0094 0000 009c 0000
0000060 009c 0000 009c 0000 009c 0000 009c 0000
0000100 009c 0000 009c 0000 009c 0000 00a4 0000
0000120 00a4 0000 00a4 0000 00ac 0000 00ac 0000
0000140 00ac 0000 00ac 0000 00ac 0000 00a4 0000
0000160 0094 0000 009c 0000 007c 0000 0074 0000
0000200 005c 0000 005c 0000 0054 0000 006c 0000

0777600 004c 0000 0044 0000 0054 0000 005c 0000
0777620 005c 0000 005c 0000 0054 0000 0054 0000
0777640 0054 0000 0064 0000 0064 0000 007c 0000
0777660 007c 0000 007c 0000 0084 0000 007c 0000
0777700 0074 0000 005c 0000 004c 0000 003c 0000
0777720 003c 0000 0034 0000 002c 0000 0024 0000
0777740 002c 0000 0034 0000 0044 0000 004c 0000
0777760 005c 0000 005c 0000 0064 0000 006c 0000

The dumpsdram.cpp was used to test the SDRAM on the XulA2-LX9 or XulA2-LX25
FPGA module. The program dumpsdram_dwt.cpp modified the program to perform the lifting step of the Discrete Wavelet Transform (DWT). The DWT requires to passes first with even samples followed with odd samples.

vidal@ws009:~/wkg/jpeg-2000-test/zipcpu$ cp dumpsdram_dwt.cpp dumpsdram.cpp

vidal@ws009:~/wkg/jpeg-2000-test/zipcpu$ make clean

vidal@ws009:~/wkg/jpeg-2000-test/zipcpu$ make

In a 2nd shell
vidal@ws009:~/wkg/xulalx25soc/trunk/bench/cpp$ ./busmaster_tb

vidal@ws009:~/wkg/jpeg-2000-test/zipcpu$ ./dumpsdram -p img_to_fpga.bin xx

When de-interleave is not performed the image appears like the image below.

vidal@ws009:~/wkg/jpeg-2000-test/zipcpu$ python rd_pass.py. This reads the file pass.bin
created when running the command ./dumpsdram -p img_to_fpga.bin xx. Then the image
test1_256_fwt.png

After pass 1 with de-interleave applied.

With the pass 1 & pass 2 and de-interleave applied. The image is ¼ the original size.

If further levels of decomposition were desired the image would be moved from the lower right hand corner to upper left hand corner and the steps above would be repeated. After the 2nd level of decomposition the image would be reduced to 64 x 64. With the 3rd level of decomposition the image would be reduced to 32 x 32.

The first approach used a 2 dim array to perform the lifting step. The current version use a 1 dim pointer to model the SDRAM data.

Testing the Compiled code

Set the PATH to ZIPCPU tools.

vidal@ws009:~$ . setzipcpuPath.sh
PATH,/home/vidal/bin:/usr/lib/lightdm/lightdm:/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin:/usr/games:/home/vidal/wkg/zipcpu/trunk/sw/install/cross-tools/bin:/home/vidal/wkg/xulalx25soc/trunk/sw

The files being tested currently are dwt_write.c called by dwt_steps.c & jpec.c
On Ubuntu the files compile & link
with the following commands
// to compile dwt_write.c zip-gcc -fno-builtin -c -O3 dwt_write.c -o dwt_write.o
// to compile dwt_steps.c zip-gcc -fno-builtin -c -O3 dwt_steps.c -o dwt_steps.o
// to link dwt_write.o dwt_steps.o zip-gcc -fno-builtin -nostdlib -O3 dwt_write.o dwt_steps.o -o dwt_steps -T xulalink.x
// to disasmble
// zipobj-dump -d dwt_steps.o
// zipobj-dump -d dwt_write.o
// zipobj-dump -d dwt_steps

// xsload --usb 0 --fpga tmp_svn_bld_bitfiles/toplevel.bit
//ziprun test_zipcpu/dwt

dwt_steps: file format elf32-zip

Disassembly of section .rocode:

00002000 <_start>:
    2000:	6a 00 00 00	LDIHI $0,SP
    2001:	6a 40 3f ff	LDILO $16383,SP
    2002:	7c 87 c0 00	LJMP @0x0000200f
    2003:	00 00 20 0f

00002004 <dwt_write>:
    2004:	68 00 00 01	SUB $1,SP
    2005:	2c c7 40 00	STO R5,(SP)
    2006:	19 80 00 08	LSL $8,R3
    2007:	2b c0 c0 00	MOV R3,R5
    2008:	08 85 40 00	ADD R5,R1
    2009:	1b c0 40 00	MOV R1,R3
    200a:	18 84 80 00	ADD R2,R3
    200b:	24 c4 c0 00	STO R4,(R3)
    200c:	2c 87 40 00	LOD (SP),R5
    200d:	68 80 00 01	ADD $1,SP
    200e:	7b c0 00 00	JMP R0

0000200f <entry>:
    200f:	68 00 00 0e	SUB $14,SP
    2010:	04 c7 40 05	STO R0,$5(SP)
    2011:	2c c7 40 06	STO R5,$6(SP)
    2012:	34 c7 40 07	STO R6,$7(SP)
    2013:	3c c7 40 08	STO R7,$8(SP)
    2014:	44 c7 40 09	STO R8,$9(SP)
    2015:	4c c7 40 0a	STO R9,$10(SP)
    2016:	54 c7 40 0b	STO R10,$11(SP)
    2017:	5c c7 40 0c	STO R11,$12(SP)
    2018:	64 c7 40 0d	STO R12,$13(SP)
    2019:	0d 80 20 8d	LDI $8333,R1
    201a:	0c c0 01 06	STO R1,($262)
    201b:	05 80 00 02	LDI $2,R0
    201c:	04 c7 40 00	STO R0,(SP)
    201d:	78 80 00 3e	BRA @0x0000205c
    201e:	14 85 80 00	LOD (R6),R2
    201f:	0c 85 82 00	LOD 512(R6),R1
    2020:	10 84 40 00	ADD R1,R2
    2021:	53 c0 80 00	MOV R2,R10
    2022:	0b c0 80 00	MOV R2,R1
    2023:	09 c0 00 01	ASR $1,R1
    2024:	2b c0 40 00	MOV R1,R5
    2025:	0c 85 81 00	LOD 256(R6),R1
    2026:	08 05 40 00	SUB R5,R1
    2027:	23 c0 40 00	MOV R1,R4
    2028:	1b c1 c0 00	MOV R7,R3
    2029:	13 c2 00 00	MOV R8,R2
    202a:	0b 00 01 00	BREV $256,R1
    202b:	03 c3 c0 02	MOV $2+PC,R0
    202c:	7c 87 c0 00	LJMP @0x00002004
    202d:	00 00 20 04
    202e:	38 80 00 02	ADD $2,R7
    202f:	30 80 02 00	ADD $512,R6
    2030:	3c 00 01 00	CMP $256,R7
    2031:	78 9b ff ec	BNZ @0x0000201e
    2032:	54 c7 40 01	STO R10,$1(SP)
    2033:	2c c7 40 02	STO R5,$2(SP)
    2034:	03 c2 00 00	MOV R8,R0
    2035:	0b 00 01 00	BREV $256,R1
    2036:	00 84 40 00	ADD R1,R0
    2037:	2b c0 00 00	MOV R0,R5
    2038:	3d 80 00 01	LDI $1,R7
    2039:	14 85 40 00	LOD (R5),R2
    203a:	0c 85 42 00	LOD 512(R5),R1
    203b:	10 84 40 00	ADD R1,R2
    203c:	53 c0 80 00	MOV R2,R10
    203d:	03 c0 80 00	MOV R2,R0
    203e:	01 c0 00 02	ASR $2,R0
    203f:	0c 85 41 00	LOD 256(R5),R1
    2040:	00 84 40 00	ADD R1,R0
    2041:	23 c0 00 00	MOV R0,R4
    2042:	1b c1 c0 00	MOV R7,R3
    2043:	13 c2 00 00	MOV R8,R2
    2044:	0b 00 01 00	BREV $256,R1
    2045:	03 c3 c0 02	MOV $2+PC,R0
    2046:	7c 87 c0 00	LJMP @0x00002004
    2047:	00 00 20 04
    2048:	38 80 00 02	ADD $2,R7
    2049:	28 80 02 00	ADD $512,R5
    204a:	3c 00 00 ff	CMP $255,R7
    204b:	78 9b ff ed	BNZ @0x00002039
    204c:	40 80 00 01	ADD $1,R8
    204d:	44 00 01 00	CMP $256,R8
    204e:	78 90 00 09	BZ @0x00002058
    204f:	0b c2 00 00	MOV R8,R1
    2050:	02 00 00 80	LDIHI $128,R0
    2051:	02 40 01 00	LDILO $256,R0
    2052:	08 84 00 00	ADD R0,R1
    2053:	33 c0 40 00	MOV R1,R6
    2054:	3d 80 00 02	LDI $2,R7
    2055:	2c c7 40 03	STO R5,$3(SP)
    2056:	54 c7 40 04	STO R10,$4(SP)
    2057:	78 83 ff c6	BRA @0x0000201e
    2058:	0c 87 40 00	LOD (SP),R1
    2059:	08 83 ff ff	ADD $-1,R1
    205a:	0c c7 40 00	STO R1,(SP)
    205b:	78 90 00 02	BZ @0x0000205e
    205c:	45 80 00 00	CLR R8
    205d:	78 83 ff f1	BRA @0x0000204f
    205e:	0a 00 00 00	LDIHI $0,R1
    205f:	0a 40 20 75	LDILO $8309,R1
    2060:	24 84 40 00	LOD (R1),R4
    2061:	1b c1 00 00	MOV R4,R3
    2062:	12 00 00 00	LDIHI $0,R2
    2063:	12 40 20 75	LDILO $8309,R2
    2064:	24 00 00 00	CMP $0,R4
    2065:	78 98 00 02	BNZ @0x00002068
    2066:	14 80 01 0f	LOD ($271),R2
    2067:	78 80 00 09	BRA @0x00002071
    2068:	0c 80 01 0a	LOD ($266),R1
    2069:	0c 00 00 00	CMP $0,R1
    206a:	78 9b ff fd	BNZ @0x00002068
    206b:	10 80 00 01	ADD $1,R2
    206c:	1c c0 01 0a	STO R3,($266)
    206d:	1c 84 80 00	LOD (R2),R3
    206e:	1c 00 00 00	CMP $0,R3
    206f:	78 9b ff f8	BNZ @0x00002068
    2070:	78 83 ff f5	BRA @0x00002066
    2071:	0c 80 01 0f	LOD ($271),R1
    2072:	14 04 40 00	CMP R1,R2
    2073:	78 93 ff fd	BZ @0x00002071
    2074:	78 83 ff ec	BRA @0x00002061

00002075 <msg>:
    2075:	00 00 00 48 00 00 00 65 00 00 00 6c 00 00 00 6c ...H...e...l...l
    2079:	00 00 00 6f 00 00 00 2c 00 00 00 20 00 00 00 77 ...o...,... ...w
    207d:	00 00 00 6f 00 00 00 72 00 00 00 6c 00 00 00 64 ...o...r...l...d
    2081:	00 00 00 21 00 00 00 0a 00 00 00 00 ...!........

Transfer the image from the host to the SDRAM of the XulA2-LX9. Since the -p option was not used. The dumpsdram connects to the XulA2-LX9. This should blink the green led on the XulA2-LX9 for several seconds.

“dumpsdram img_to_fpga.bin xx”

Run the dwt_steps C program.

“ziprun dwt_steps”

“wbregs cpu 0”

Use the zipdbg to step through the code.