Tristate fom Dave Vandenbout
05/09/16
def tristate_driver(o, i, enbl):
        ''' Tristate driver module.
        o: 3-state output (high, low, Z). Must be declared TriStateSignal().
        i: input.
        enbl: When low, o is Z, otherwise o is i.
        '''

        o_drvr = o.driver() # Get ShadowSignal for driving output.

        @always_comb
        def drvr_logic():
        if enbl == 1:
        o_drvr.next = i # Drive output with value on input.
        else:
        o_drvr.next = None # Equivalent to Z.

        # Dummy signal driven by o so MyHDL recognizes it as an inout.
        dummy = Signal(bool(0))

        @always_comb
        def dummy_logic():
        dummy.next = bool(o)

        return instances()
    # Attach tristate drivers. The bits where drvr_enbls has 1s will be enabled,
    # while the rest will be Z. Of the enabled bits, the bit driving the anode
    # of the active digit will be high and the rest (connected to the cathodes)
    # will be low.
    d = [d0_o, d1_o, d2_o, d3_o, d4_o, d5_o, d6_o, d7_o]
    for i in range(len(d)):
        inst.append(tristate_driver(d[i], digit_shf(i), drvr_enbls(i)))

    return instances()

always @(disp_digit_shf[1], disp_drvr_enbls[1]) begin: CATBOARD_DISP_INST_2_DRVR_LOGIC
    if ((disp_drvr_enbls[1] == 1)) begin
        disp_inst_2_o_drvr = disp_digit_shf[1];
    end
    else begin
        disp_inst_2_o_drvr = 'bz;
    end
end

always @(disp_digit_shf[1], disp_drvr_enbls[1]) begin: CATBOARD_DISP_INST_2_DRVR_LOGIC
    if ((disp_drvr_enbls[1] == 1)) begin
        disp_inst_2_o_drvr = disp_digit_shf[1];
    end
    else begin
        disp_inst_2_o_drvr = 'bz;
    end
end